## Slide 1: The role of in-use PEMS testing to ensure regulatory compliance and policy effectiveness … and to avoid another Volkswagen crisis.
Nick Molden
17 March 2016

## Slide 2: Emissions Analytics’ credentials
  Founded in 2011
  Headquartered in UK, with operations in London, Los Angeles and Stuttgart
  Specialist in PEMS testing and data analysis
  1200+ vehicles tested
  Largest commercially available database of real-world emissions data
  Works with OEMs, Tier 1/2 suppliers, fuel and chemical companies, regulators, consultancies, consumer media

## Slide 3: Equipment
SEMTECH-DS and -LDV
Portable Emissions Measurement System connects to tailpipe
    Captures emissions for CO2, CO, NO, NO2, total hydrocarbons
    At 1 Hertz
  Air temperature, pressure, humidity
  GPS for speed and altitude
  Engine data via CANBUS
  Fuel economy derived via carbon balance
  Weight addition 100-250 pounds

## Slide 4: Objectives
  Rolling in-service surveillance programme of production vehicles
  Target to test 500+ vehicles per year
  To complement type approval
  And ensure efficacy of regulations
  Air quality, greenhouse gases, fuel economy
  Independent, making data available to all
  Top-level ratings for marketing
  Benchmark rankings
  Deep-dive analysis for manufacturers

## Slide 5
TRACKING POLICY EFFECTIVENESS

## Slide 6
Rolling 12-month average of exceedance factor in blue
Step-change technology launched Q2 to Q3 2014
No further reduction in Conformity Factor since then
Average CF dipped to 2.7 in 2014, but risen to 3.5 since then
NOx latest trends (1)

## Slide 7
German manufacturers leading introduction of Euro 6 vehicles
And offer the cleanest
US manufacturers slow to bring Euro 6 vehicles to market
Japanese very consistent around market average conformity factor
NOx latest trends (2)

## Slide 8
Earliest Euro 6 vehicles were LNT and EGR-only, but LNT quickly became dominant technology
More recent switch to SCR
Nevertheless, good performance achieved by many LNT systems
Similarly wide spread of performance between LNT and SCR
NOx latest trends (3)

## Slide 9
Conformity factor initially 2.1 – 168 mg/km
Further increased by exclusions due to boundary conditions – details TBD
PEMS test-to-test variability of 30%, so OEMs will need to target ~129 mg/km to avoid getting caught by in-service surveillance
Will Real Driving Emissions help?

## Slide 10
Fuel economy by country

## Slide 11
TRACKING VEHICLE PERFORMANCE

## Slide 12: Segment/fuel ranking

## Slide 13: Drill-down to individual datasets

## Slide 14
INDEPENDENT AIR QUALITY RATINGS

## Slide 15: Vehicle rating scheme
  Vehicle rating scheme based on their real-world NOx emissions, launching in April 2016
  Initially on cars, but shortly to extent to light commercial vehicles
  Non-statutory complement to new Real Driving Emissions regulations
  But will also
      Discriminate between high and low emitters, rather than just pass/fail
      Be updated for each model year to keep up with new calibrations
  Ratings will be published and put in the public domain
  Manufacturers and consumer media can adopt as independent, voluntary standard
  Similar to New Car Assessment Programme (Euro NCAP, Global NCAP)
  Robust, independent standard needed to measure and incentivise actions to bring about air quality improvements

## Slide 17
Nick Molden, Chief Executive Officer
nick@emissionsanalytics.com
+44 (0) 20 7193 0489
+44 (0) 7765 105902