## Slide 1: Estimating Total Particle Formation Using Environmental Chambers
David Cocker
UC Riverside/CE-CERT
March 18, 2016

## Slide 2: Traditional Environmental Chambers
Laboratory chambers are indispensable in the study of gas-phase atmospheric chemistry and atmospheric aerosol formation and growth. Because of the difficulty of isolating chemical and microphysical processes in the atmosphere from flow and mixing effects, chamber studies provide the means to develop mechanistic understanding of such processes. In this context, a laboratory chamber constitutes a well-mixed batch reactor in which the chemical processes of interest can be isolated directly.

## Slide 3: Carter et al., 2006, Mechanism Conference, http://www.cert.ucr.edu/~carter/Mechanism_Conference/17%20C%20carter.pdf )

## Slide 4
Hallquist et al., 2009, ACP:9, 5155-5236

## Slide 5: Indoor vs. Outdoor
Pros (Outdoor) – Natural sunlight provides full spectrum of wavelengths; allows for photolysis of more products
Con (Outoor) – Difficult to control photolysis due to changes in weather, clouds, etc. makes replication of experiment difficult; temperature and relative humidity are dictated by environment and will fluctuate during course of experiment

## Slide 6: Select Chambers

## Slide 7: SAPHIR
Simulation of Atmospheric PHotochemistry In a large Reaction (SAPHIR) chamber in Jülich, Germany (http://www.eurochamp.org/chambers/saphir/): 270 m3

## Slide 8: UCR Chamber Facility

## Slide 9: UC Riverside/CE-CERT Environmental Chamber
Dual 90 m3 Teflon reactors
Descending frames to maintain positive pressure
Purified air flushed 450 m3 enclosure
Injection and sample ports
Dual SMPS’s
Particle free two chamber humidifier
Air handler circulation system
TDMA – Hygroscopicity Measurement
Argon arc lamp
Black lights

## Slide 10: EUPHORE
EUPHORE (European PHOtoREactor) chamber in Valencia, Spain (http://www.eurochamp.org/chambers/euphore): volume = 200m3 each.

## Slide 11: Chemical Instrumentation
+
VOCs
Oxidants
Products (aerosol)
Products (gases)
GC-FID
PTR-MS
Intermediates
LCMS
AMS
GCxGC
IR-CRDS
CRDS

## Slide 12: Aerosol Instrumentation
Atmospheric reactor
SMPS
(Size
Distribution)
CPC
(Number
Concentration)
APM
(Single
Particle Mass)
(CCN)
Cloud particle activation
SOA
Aerosol Mass Produced
TDMA
(hygroscopicity
volatility)
AMS
(Chemical
composition)

## Slide 13: Indoor vs. Outdoor
Pros (Indoor) – Can de designed for excellent temperature and RH control, repeatable photolysis conditions
Cons (Indoor) – Difficult to simulate natural sunlight across the solar spectrum – relative rates of photolysis may be affected

## Slide 14: Comparison of Light Spectra
Carter et al., 2004, ARB report
http://www.cert.ucr.edu/~carter/pubs/lnoxrpt.pdf

## Slide 15: k1 measurement
NO2 photolysis rate k1
(NO2) = (NO2)final + ½ Δ(NO)
F: total flow rate in reactor
V: volume of quartz reactor
φ: quantum yield for the production of nitric oxide
T: overall transmission factor of the quartz tube for UV light
known volume quartz tube
hν
NO2
1.00 L/min
NOX
Analyzer

## Slide 16: Primary vs. Secondary Particulate
Primary (direct) particulate emissions – defined by source and measurement method
(Focus of PEMS conference)

## Slide 17
Kittelson, 2008, AQMD Ultrafine Conference

## Slide 18: SOA from POA?
Robinson et al., 2007, Science
Significant fraction of POA volatilize at higher dilution ratio (~ambient condition)
Traditional SOA precursors cannot explain SOA from diesel exhaust
SOA from “Intermediate/Semi”-volatility Organic Compounds (IVOCs, SVOCs)

## Slide 19: Primary vs. Secondary Particulate
Primary (direct) particulate emissions – defined by source and measurement method
+ NOx
(Also focus of PEMS conference)

## Slide 20: Primary vs. Secondary Particulate
Primary (direct) particulate emissions – defined by source and measurement method
+ NOx
+ organic vapors

## Slide 21: Primary vs. Secondary Particulate
Primary (direct) particulate emissions – defined by source and measurement method
+ NOx
+ organic vapors
+ ammonia

## Slide 22: Primary vs. Secondary Particulate
Primary (direct) particulate emissions – defined by source and measurement method
+ NOx
+ organic vapors
+ ammonia
Gases undergo subsequent reaction in the atmosphere leading to the formation of additional particulate referred to as secondary particulate

## Slide 23: Atmospheric Chemistry Takes Over
Organic vapors + NOx + sunlight  ozone

## Slide 24: Atmospheric Chemistry Takes Over
Organic vapors + NOx + sunlight  ozone
AND Organic vapors with decreasing vapor pressure (condensable vapors)

## Slide 25: Atmospheric Chemistry Takes Over
Organic vapors + NOx + sunlight  ozone
AND Organic vapors with decreasing vapor pressure (condensable vapors)
AND Nitric acid

## Slide 26: Atmospheric Chemistry Takes Over
Organic vapors + NOx + sunlight  ozone
AND Organic vapors with decreasing vapor pressure (condensable vapors)
AND Nitric acid
AND Ammonium nitrate (if ammonia present)

## Slide 27: Inorganic Secondary Particulate
NO + ozone
NO2
.OH
HNO3
NH3
NH4NO3
Similarly,
SO2 + oxidant
SO3
H2O
H2SO4
NH3
(NH4)2SO4

## Slide 28: Secondary Organic Aerosol
Organic gases
+ .OH
Lighter
(fragmentation)
Oxidation
Products
Heavier (functionalization) Oxidation Products
+
Sorption
Evaporation

## Slide 29: Chemistry of SOA Formation is Complicated!
VOC
Plus additional SOA formation through oligomerization …

## Slide 30: Primary/Secondary Organic Aerosol
Organic gases
Lighter
(fragmentation)
Oxidation
Products
Heavier (functionalization) Oxidation Products
+
Sorption
Evaporation (due to
dilution)
+
.OH

## Slide 31: How do we look at SOA Formation?
SOA formation is driven by gas-to-particle partitioning, with the gas-to-particle partitioning coefficient defined as:
saturation liquid vapor pressure
activity coefficient

## Slide 32: Equilibrium Partitioning of Semi-Volatile Compounds
A1, A2,…,An
G1, G2,…,Gn
Kom,i
=
Ai/Mo
Gi
=
MWomgipoL,i
RT
gi = gi(x1,x2,…,xn)
poL,i = poL,i (T)
ROG
a1(DROG)
a2(DROG)
…
an(DROG)

## Slide 33: SOA formation potential
0
2
4
6
8
10
12
0
100
200
300
400
500
600
Time (minute)
Volume (
m
m
3
/cm
3
)
0
10
20
30
40
50
60
HC (ppb)
PM Volume(corrected)
PM Volume(uncorrected)
Hydrocarbon
DROG
DMo

## Slide 34
At small Mo
SOA formation as a function of organic aerosol mass

## Slide 35: General SOA Experimental Protocol
DROG
DMo
Yexpt
Ycalc
Kom,i
ai
--Coefficients Kom.i and ai values are then varied so that the sum of the residuals between experimental and calculated yields for a single parent is minimized.
--Assume two product classes
Parent ROG(s)
Seed Aerosol (optional)
Propene (optional)
NO, NO2
Gas Phase Sampling:
-Hydrocarbon
-Ozone, NO, NO2
-Relative humidity, T
Aerosol Sampling:
-Number Concentration
-Size Distribution

## Slide 36: SMPS
-
-
-
-
-
-
-
-
-
-
Sheath
Excess
(To detector)
Filter
Filter
Charger
DMA
CNC
To pump
Aero
Mono
From
Chamber

## Slide 38: VTDMA Volatility Tandem Differential Mobility Analyzer
+
+
+
+
-
-
-
-
+
+
+
Electrical
force
Drag
force
DMA
Thermal
denuder
particle with
specific size
SMPS
size scan
Residence
chamber
HTDMA Hygroscopicity Tandem Differential Mobility Analyzer
Notes: The volatility of the SOA is continuously measured using a (VTDMA) .A monodisperse aerosol fraction is selected by the first DMA. The particles of specific size goes into a thermodenuder with a temperature setting of 100 C and residence time of 16 sec. Then the change in particle diameter is detected by a SMPS system.
It can determine the Volume remaining fraction by this equation. The VTDMA system is used to detect possible changes in the volatility of SOA with aging time.

## Slide 39
TDMA analysis (volatility or hygroscopicity)
Gf=Df/Di or VRF=(Di/Df)3

## Slide 40: General Emission Protocol
DROG
DMo
Yexpt
Ycalc
Kom,i
ai
--Coefficients Kom.i and ai values are then varied so that the sum of the residuals between experimental and calculated yields for a single parent is minimized.
--Assume two product classes
Vehicle exhaust
Propene (optional)
H2O2 (optional)
Gas Phase Sampling:
-Hydrocarbon
-Ozone, NO, NO2
-Relative humidity, T
Aerosol Sampling:
-Number Concentration
-Size Distribution
-Chemical Composition
-Fractal Dimension

## Slide 41
Gordon et al., www.atmos-chem-phys.net/14/4661/2014/

## Slide 42: Why fractal dimension matters
Condensing organic material will fill voids while potentially not changing mobility diameter
Must be careful to not use SMPS only and assume constant density
Shape of primary aerosol influenced by dilution….

## Slide 43: Particle measurement methods
1. SMPS
- volume (based on dm)
2. APM – SMPS
- mp, dm  ρeff
3. HR-ToF-AMS
Non refractory organics
dm: mobility diameter
mp: mass of particle
ρeff: effective density
SMPS: Scanning Mobility Particle Sizer
APM: Aerosol Particle Mass Analyzer
HR-ToF-AMS: High Resolution-Time-of-Flight Aerosol Mass Spectrometer

## Slide 44
Higher resolution for W mode
Higher sensitivity for V mode
inlet
Electronic box
Power Supply
TPS Box
HR-ToF-AMS Aerodyne High Resolution Time-of-Flight Aerosol Mass Spectrometer
Source: DeCarlo et al., 2006

## Slide 45: Measurement of SOA by AMS
Run 1 (engine idle,short transfer line, DR: 114)
C4H9+: tracer of primary organic aerosol*
POA
SOA
*Chirico et al. 2010, APCD

## Slide 46: Measurement of SOA by AMS
Nakao et al. (2011) AS&T
Robinson et al. (2007) Science

## Slide 47
Gordon et al., www.atmos-chem-phys.net/14/4661/2014/

## Slide 48
Gordon et al., www.atmos-chem-phys.net/14/4643/2014/

## Slide 49: Challenges
Oxidizing environment controlled by exhaust gases (organics and NOx)
Limited oxidation time
Wall effects can be important (loss of SOA precursor gases to walls, interaction of sorbing gases to particles on the surface)

## Slide 50: Chemistry of SOA Formation is Complicated!
VOC
Plus additional SOA formation through oligomerization …

## Slide 51: Kinetics very important
d[C]/dt = k[A][B]
RO2 + HO2  heavier oxidation product (e.g., hydroperoxide)
d[oxidation product]/dt = k[.RO2][.HO2]
NO competes for .RO2 and .HO2
  [.RO2] and [.HO2] very dependent on [NO] as NO quickly reacts with .RO2 and .HO2 to form .RO and .HO.

## Slide 52
VOC
Plus additional SOA formation through oligomerization …

## Slide 53: Sample Gas Phase and PM Trace
Chart: Time (min)
NO2/NO | 0.068015 | 0.061588 | 0.043768 | 0.10551 | 0.11748 | 1.7491 | 2.0877 | 18.8033 | 21.266 | 51.9087 | 48.7904 | 87.3603 | 87.7483 | 164.1032 | 282.716 | 234.7845 | 154.5994 | 195.9484 | 200 | 201.421 | 253.979 | 260 | 292.2366
Chart: Time (min)
NO2/NO | 0.068015 | 0.061588 | 0.043768 | 0.10551 | 0.11748 | 1.7491 | 2.0877 | 18.8033 | 21.266 | 51.9087 | 48.7904 | 87.3603 | 87.7483 | 164.1032 | 282.716 | 234.7845 | 154.5994 | 195.9484 | 200 | 201.421 | 253.979 | 260 | 292.2366

## Slide 54: Sample Gas Phase and PM Trace
Chart: Time (min)
NO2/NO | 0.068015 | 0.061588 | 0.043768 | 0.10551 | 0.11748 | 1.7491 | 2.0877 | 18.8033 | 21.266 | 51.9087 | 48.7904 | 87.3603 | 87.7483 | 164.1032 | 282.716 | 234.7845 | 154.5994 | 195.9484 | 200 | 201.421 | 253.979 | 260 | 292.2366
Chart: Time (min)
NO2/NO | 0.068015 | 0.061588 | 0.043768 | 0.10551 | 0.11748 | 1.7491 | 2.0877 | 18.8033 | 21.266 | 51.9087 | 48.7904 | 87.3603 | 87.7483 | 164.1032 | 282.716 | 234.7845 | 154.5994 | 195.9484 | 200 | 201.421 | 253.979 | 260 | 292.2366

## Slide 55: Comparison of Two Experiments with the Same Initial and Reacted m-Xylene Concentrations
Initial NOx: 266 ppb
Initial NOx: 9 ppb

## Slide 56: Example of how NOx influences SOA yield
Experiments with increasing NOx

## Slide 58: So how do we best mimic atmosphere
Clearly SOA formation is driven by the gas-phase chemistry leading to oxidation of organic vapors, which in turn, can condense/sorb into existing organic matter.
Option 1a: Inject gases and particles directly from tailpipe (after dilution and cooling) and turn on lights. Gas-phase chemistry will be dominated by organic gases and NOx from vehicle
Option 1b: inject organic gases and particles into system with surrogate atmosphere (e.g., VOC dominated by anthropogenic or biogenic sources) already present
Option 1c: reduce NOx during injection into chamber
Option 1d: Alter reactivity of system by injecting propene, H2O2, HONO or other species.
Option 2: Mimic total oxidation of atmosphere on days scale in short time by elevating oxidants. (PAMS)

## Slide 59: Option 2: PAMS

## Slide 60: Photochemical Measurement
Example PAM reactor setup/applications (from T.B. Onasch et al., DoE ASR Meeting, Spr 2012).

## Slide 61: PAMS system

## Slide 62
Advantages: - Wider range of oxidant exposure time (1–30 days vs. 1 day) - Shorter experiment duration (minutes vs. hours or days) Disadvantages: - High OH concentrations required to simulate atmospherical aging timescales (1010 - 1012 vs. 106 - 107 molec cm-3) - High (parts-per-million) levels of O3 required for OH production - UV emission spectrum different than troposphere (peak λ = 254 nm vs λ > 300 nm)

## Slide 63
Tkacik et al., Environ. Sci. Technol. 2014, 48, 11235−11242
OH exposures ranged from 7.4 × 1010 to 2.4 × 1012 molecules cm−3 s or approximately 0.3−9.3 days of equivalent photochemical aging at a typical urban OH concentration of 3 × 106 molecules cm−3

## Slide 64
VOC
Plus additional SOA formation through oligomerization …

## Slide 65
At small Mo
SOA formation as a function of organic aerosol mass

## Slide 66: So what did we learn?
How environmental chambers and PAMS used to study secondary aerosol formation
Difficulties in simulating atmosphere and interpreting results
  Regardless of measurement challenges, secondary PM formation clearly important and may dominate PM from engines in many situations with respect to atmospheric particle mass loadings
Need to better mimic atmospheric processes

## Slide 67: Come by for tour!

## Slide 68
Donahue et al., AAAR, 2010