## Slide 1
High-Speed Portable FTIR Measurements From In-Use Heavy-Duty CNG Transit Buses
PEMS International Conference & Workshop April 3-4, 2014
Xu Wang1, Saroj Pradhan2, Arvind Thiruvengadam2,
Marc Besch2, David Quiros1, Tao Huai1
1 Monitoring & Laboratory Division, California Air Resources Board
2 Center for Alternative Fuels, Engines & Emissions, West Virginia University

## Slide 2
Motivation and Background
Transit buses are commonly powered by compressed natural gas (CNG); designed to meet the 2010 NOX standard (0.2 g/bhp-hr) with a simple three-way catalyst (TWC).
However, under certain conditions, stoichiometric CNG buses with a TWC can favor emissions of ammonia (NH3) and nitrous oxide (N2O) affecting secondary PM formation and global climate, respectively.
Laboratory measurements of NH3, and other unregulated pollutants, have been conducted in the controlled laboratory.
On-road measurements of many gaseous pollutants is possible with a portable FTIR instruments (PEMS), but further evaluation needed.

## Slide 3: Objectives
Compare emissions measured over DYNAMOMETER and two ON-ROAD routes for the same stoichiometric TWC-equipped CNG urban transit buses during operation in a typical CA city.
Evaluate the performance of a portable FTIR, the MKS 2030 HS, in reference to CFR 1065 compliant measures.
Using a portable FTIR, report emission factors for: ammonia (NH3), nitrous oxide (N2O), and methane (CH4).
West Virginia University
Transportable Emissions Measurement System (TEMS)
Sacramento Regional Transit Bus
PEMS for on-road measurement

## Slide 4: Study Design: 3 routes, 3 buses 2008 Cummins Westport ISL-G Stoichiometric CNG with TWC
OC BUS Cycle Orange County Bus Cycle Transportable Dynamometer | In-use LOCAL Route Sacramento RT #51 (with all regular stops) | In-use HIGHWAY Route Sacramento RT #7 (with all regular stops)
Distance: 6.5 mi Time: 2000 sec 11.7 mph Bus A & Bus B | Distance: 11 mi Time: 3000 sec 13.3 mph Bus B & Bus C | Distance: 9 mi Time: 1000 sec 32.4 mph Bus B & Bus C
WVU 1065-compliant Transportable Emissions Measurement System: NO, NOX, CO, CO2, CH4, THC, NMHC MKS 2030HS FTIR: CO, CO2, NO, NO2, CH4, NH3, N2O | Horiba OBS 2200: CO, CO2, NO, NO2, NOX MKS 2030 HS FTIR: NH3, N2O, CH4 | 
B

## Slide 5: Gaseous Emissions by Driving Cycle
Chart: Emission Factor [g/mi]
| CO2 /1000 | NO | NOX | CO /100
OC Bus (TEMS) | 2.7266 | 0.77541 | 0.78115 | 0.60573
Local (OBS-2200) | 1.8306 | 0.81305 | 0.83977 | 0.2324
Highway (OBS-2200) | 1.0316 | 0.69088 | 0.70082 | 0.1648
CO2, /1000
NO
NOX
CO /100

## Slide 6: Verification of the FTIR with TEMS (Dynamometer Cycle)
Chart: Emission Factor [g/mi]
| CH4 / 10 | NO | NOX | CO /100 | CO2 /5000
TEMS | 0.61789 | 0.77541 | 0.78115 | 0.60573 | 0.54531
FTIR | 0.68483 | 0.74007 | 0.76144 | 0.53179 | 0.59259
CO2 /5000
NO
NOX
CO /100

## Slide 7
Portable FTIR: Real-Time NH3, BUS B
Dynamometer
Max: 1040 ppm
Average: 145 ppm
On-road LOCAL
Max: 1062 ppm
Average: 155 ppm
On-road HIGHWAY
Max: 986 ppm
Average: 208 ppm

## Slide 8: Portable FTIR: Real-Time N2O, BUS B
Vehicle Speed (mph)
N2O (ppm)
N2O (ppm)
N2O (ppm)
Vehicle Speed (mph)
Vehicle Speed (mph)
Dynamometer
Max: 42 ppm
Average: 1.19 ppm
On-road LOCAL
Max: 32 ppm
Average: 0.54 ppm
On-road HIGHWAY
Max: 57 ppm
Average: 3.09 ppm

## Slide 9
Chart: Emission Rate [mg/sec]
Chart: Speed [mph]
Bus B
Bus C
Highway Route: N2O Emissions Vary Between Buses Tested Over Same In-Use Route

## Slide 10
On-Road HIGHWAY: Weak Relationship Between
Road Load (Power) and Emission Rate
Chart: NH3
Chart: N2O

## Slide 11: Portable FTIR: NH3, N2O and CH4 Emission Factors
Chart: Emission Factor [g/mi]
| NH3 | CH4 | N2O x100
Dyno (OC Bus) | 3.0638 | 6.8483 | 1.5701
Local | 1.7133 | 6.0407 | 3.9303
Highway | 1.0083 | 3.7444 | 8.2458
NH3
CH4
N2O (x100)

## Slide 12: Comparison of CNG Emission Factors
Configuration | CO2 (kg/mi) | NOX (g/mi) | CH4 (g/mi) | NH3 (g/mi) | N2O (mg/mi)
This study, OC BUS | 2.7 | 0.78 | 6.9 | 3.1 | 16
This study, on-road LOCAL | 1.8 | 0.84 | 6.0 | 1.7 | 39
This study, on-road HIGHWAY | 1.0 | 0.70 | 3.7 | 1.0 | 83
CNG Buses w/TWC, UDDS1 | 1.7 | 0.52 | 3.5 |  | 
CNG Buses w/TWC, 45 mph1 | 0.7 | 0.11 | 1.3 |  | 
CNG Buses w/OC (Lean), UDDS1 | 1.5 | 14.9 | 6.4 |  | 
HD CNG w/TWC2 |  | 0.15* |  | 1.2* | 
LD CNG w/TWC, FTP3 |  |  |  |  | 25-85
HD CNG4,5 |  |  |  |  | 36-93
Yoon, S. et al. Criteria pollutant and greenhouse gas emissions from CNG transit buses equipped with three-way catalysts compared to lean-burn engines and oxidation catalyst technologies. JAWMA 63(8):926–933, 2013.
Johnson, K. Emissions from In-Use NG, Propane, and Diesel Fueled Heavy Duty Vehicles. DEER 2011.
Vanderlei Borsari & João Vicente de Assunção, Nitrous oxide emissions from gasohol, ethanol and CNG light duty vehicles, Climatic Change (2012) 111:519–531
Graham, L.A. et al. Greenhouse gas emissions from heavy-duty vehicles. Atmospheric Environment 42 (2008) 4665–4681.
Becker, et al. Nitrous Oxide (N2O) Emissions from Vehicles. ES&T. 1999, 33, 4134-4139.
*Average of UDDS, CBD, and Cruise Cycles, converted using 3 bhp-hr = 1 mi.

## Slide 13: Key Findings
NH3 and CH4 emission factors scale with CO2 emissions (OC BUS > ON-ROAD), but N2O emission factors exhibit opposite trend: 2-4 times higher for local and highway ON-ROAD routes than OC BUS.
Real-time emissions of NH3 and N2O poorly explained by engine output alone; and test-to-test, or bus-to-bus, variability was observed.
Six tests from three buses over three routes show FTIR emissions of NH3, CH4, and N2O were within broad literature ranges.
Future use of portable FTIR as a PEMS warranted for measuring a diverse array of regulated and unregulated gaseous pollutants.