## Slide 1
Real World Emissions Testing Based on FTIR Technology
PEMS Conference 2014
Ron Tandy
Acknowledgements (Data Provided):
Hong Kong EPD – Carol Wong
West Virginia University – Arvind Thiruvengadam

## Slide 2: Contents
What is FTIR
FTIR Technology Explained
Features and Benefits of FTIR for Automotive and PEMS use
FTIR Accuracy and Correlation (Real World Data)
Conclusions

## Slide 3: What is FTIR
Multi-component gas analyzer based on
Fourier Transform Infra-Red technology.
Current FTIR technology allows for the continuous measurement of up to 40 gases, at 5Hz data acquisition and fast response time, makes an FTIR the ideal instrument for the R&D of engines, aftertreatment calibration, and catalytic converters.
(Not your daddy’s FTIR from 15-30 years ago)

## Slide 4: Interferometer Technology
Michelson Interferometer creates interfering beams using
IR Light source
Beam splitter
Moving mirror
Fixed mirror
A Helium Neon (HeNe) Laser determines mirror position, velocity and travel direction (Used to control mirror velocity)
The output is a Interferogram, containing information about all wavenumber frequencies within the mid-infrared spectral range (~625 to ~6000 cm-1)
Sample Cell
Notes: Wavenumber - reciprocal of actual wavelength of light

## Slide 5: Sample Gas Cell
Multi-reflection Heated Sample Cell
Heated to 191° C
  Prevents condensation
5.1m Path
For high sensitivity
200 mL cell volume
  For fast response time
5.1 meter path (32 passes)
GAS
GAS
(Interferogram)

## Slide 6: Frequency Absorption
Detector
Each molecule has a specific Infrared frequency where it absorbs the IR radiation (bending, stretching, twisting , vibrating , etc. the molecule).
Because of the constructive (and destructive) interfering beams, the detector can read information about every wavelength in the infrared range simultaneously.
The interfering beams travel through the sample gas, where some energy is absorbed by gas molecules and some is transmitted to the detector.
The transmitted portion (not absorbed) reaches the
detector.
The absorbed portion does not reach the detector, and is directly proportional to the amount of gas molecules in the sample.

## Slide 7: Inteferogram to Gas Concentration
Interferogram
Single Beam
Absorbance Spectrum
Method Analysis
Fourier Transform
algorithm
Remove
Background
A= -Log(I/Io)
Spectrum Analysis
Method Determination
(Gas, Diesel, Etc.)
Analysis of absorption regions
Speciation of gases
Signal as a function of time
Signal as a function of frequency

## Slide 8: FTIR System Configuration (Vacuum)
Spectrometer
Heated Filter
Heated Line
Conditioning Unit
24 VDC *
LAN
Sample
Purge / B.G.
N2 / Zero Air
PC
LAN
Power
Conditioning
Sample
Conditioning
Gas Handling
Cell Pressure Control
Span Gas
Span / Audit
Audit Gas
Heated Line
Waste
110 VAC
120 VAC
or
Communication
Hub
* PEMS Version Only

## Slide 9: Sampling Rate
The FTIR spectrometer can sample at selectable rates, up to 5 Hz.
5 Hz sampling rates provide superior transient sampling, capturing more data fluctuations than 1 Hz.

## Slide 10: Benefits of FTIR - One Instrument
NDIR
NDUV / CLD
GC FID
Impinger Systems
Dry to Wet Conversion
CVS / Dilute
Laser Diode or QCL
Time Align Gas Instruments
Cutter FID
Daily Calibrations
Linearization
Drift Correction
(of gases)
Replaces
Doesn’t Require

## Slide 11: Benefits of FTIR- One Instrument
Raw data files can be reprocessed with a modified gas analysis method
No need to repeat the actual test.
Gas analysis methods for different fuel types
Measures up to 40 Gases Synchronously with one detector:
(already time aligned)
Raw measurements:
Avoids additional error posibilities from dilute measurements
Fast data acquisition, and time response

## Slide 12: Measuring Gases
Measurement of all gases absorbing in the Mid Infra-Red Spectral Range
Measurement of all regulated gas components*
Multiple and customizable ranges for many gases (e.g. COLow and COHigh).
Future-proof analyzer will measure gases of future concerns
*THC is calculated (sum of HC’s) and based upon a FID correlation factor
Gas | Formula |  |  | Concentration |  | Units
REGULATED COMPONENTS: |  |  |  |  |  | 
Carbon Monoxide (Low) |  | CO (L) | 0 - 5000 |  |  | ppm
Carbon Monoxide (High) |  | CO (H) | 0 - 8 |  |  | %
Carbon Dioxide (Low) |  | CO2 | 0 - 4 |  |  | %
Carbon Dioxide (High) |  | CO2 | 0 - 20 |  |  | %
Oxides of Nitrogen |  | NOX | Calculated (sum of NO, NO2) |  |  | 
Hydrocarbons |  | HC | Calculated (sum of Carbons) |  |  | 
Nitrous Oxide (Low) |  | N2O (L) |  |  | 0 - 100 | ppm
Nitrous Oxide (High) |  | N2O (H) |  |  | 0 - 300 | ppm
NON-REGULATED COMPONENTS: |  |  |  |  |  | 
Nitrogen Oxide (Low) |  | NO (L) | 0 - 300 |  |  | ppm
Nitrogen Oxide (High) |  | NO (H) | 0 - 3000 |  |  | ppm
Nitrogen Dioxide (Low) |  | NO2 (L) | 0 - 100 |  |  | ppm
Nitrogen Dioxide (High) |  | NO2 (H) | 0 - 1000 |  |  | ppm
Ammonia |  | NH3 |  |  | 0 - 500 | ppm
Formaldehyde |  | HCHO |  |  | 0 - 1000 | ppm
Ethanol |  | C2H6O |  |  | 0 – 1000 | ppm
Methane |  | CH4 |  |  | 0 - 2000 | ppm
Water |  | H2O |  |  | 0 - 30 | %
Acetaldehyde |  | MeCHO (CH3CHO) |  |  | 0 - 1000 | ppm
Sulfur Dioxide |  | SO2 |  |  | 0 - 1000 | ppm
Isocyanic Acid |  | HNCO |  |  | 0 - 1000 | ppm
Formaldehyde |  | HCHO |  |  | 0 - 1000 | ppm
Hydrogen Cyanide |  | HCN |  |  | 0 - 1000 | ppm
Methanoic Acid |  | HCOOH |  |  | 0 - 1000 | ppm
Carbonyl Sulfide |  | COS |  |  | 0 - 200 | ppm
DIFFERENTIATED HYDROCARBONS: |  |  |  |  |  | 
Methane |  | CH4 |  |  | 0 - 2000 | ppm
Acetylene |  | C2H2 |  |  | 0 - 1000 | ppm
Ethylene |  | C2H4 |  |  | 0 - 1000 | ppm
Ethane |  | C2H6 |  |  | 0 - 1000 | ppm
Propylene |  | C3H6 |  |  | 0 - 1000 | ppm
Propane |  | C3H8 |  |  | 0 - 1000 | ppm
Butadiene |  | C4H6(1-3C4H6) |  |  | 0 - 1000 | ppm
Butane |  | NC4 (C4H10) |  |  | 0 - 1000 | ppm
Octane |  | NC8 (C8H18) |  |  | 0 - 1000 | ppm

## Slide 13: Evaluation by Regulatory Agencies
40 CFR Part 1065:
System Response Linearity Verification Accuracy, Repeatability, Noise Interference Verification
40 CFR §1065.308 40 CFR §1065.307 40 CFR §1065.305 40 CFR §1065.375
*1065 only specifies N2O for FTIR measurement, but we also verify for many other components.
Meets or Exceeds US EPA and European Regulations

## Slide 14: PEMS FTIR Application
Vibration dampening system
Environment control box
Charge indicator with alarm
Pressure control system
Road vibration
Pressure changes (altitude)
Weather conditions
Battery charge level
Solution
Problem
AC power availability
DC power inlet (24V)
Size / Weight
Redesign under evaluation

## Slide 15: On-Board Vibration Dampening

## Slide 16: Typical PEMS Components
GPS Acquisition Unit and Software
Allows for GPS data (latitude, longitude altitude and speed), to be recorded and time-aligned with the emissions data.
ECU Acquisition Unit and Software
Allows for the vehicle ECU data to be recorded and time-aligned with the emissions data.
Video Camera Monitoring System and Software
Allows for live on-road video recording, time aligned with emissions data, GPS and ECU vehicle data .

## Slide 17: PEMS FTIR In-Use
Hong Kong EPD Testing
Coach Vehicle
Tsing Yi – Stop & Go . 7.14L Diesel
12-DEC-2012
Double Decker Bus
Kowloon – Urban
10.8L Diesel
08-JAN-2013
“one of the most dense
streets in the world”

## Slide 18: In-Use Hong Kong Coach
Gaseous Measurement A&D PEMS FTIR and SEMTECH-DS
HK-EPD Defendable Data Methods:
SEMTECH-DS: 1065 Verification Tests current
1065 In-use recommendations (e.g. drift corrections, etc.)
Linearize, Span (2) and multiples Audit’s (3 hour interval)
Algorithm based on concentrations from vehicle pre-test (3 values)

## Slide 19: Hong Kong Coach - Data
NOX Agrees*
FTIR Readings Slightly Larger
5Hz vs 1Hz
(higher transient peaks)?
FTIR has more flow?
NDIR Chiller Loss?
(5% allowed per 1065.376)
*SEMTECH-DS wet (Calculated)

## Slide 20: Hong Kong Coach - Data

## Slide 21: Hong Kong Coach - Data
CO2 Agrees*
*DS Wet (Calculated)

## Slide 22: Hong Kong Coach - Data

## Slide 23: Hong Kong Coach - Data
CO Peaks Generally Agree
FTIR Peaks are larger
5Hz vs 1Hz
(higher transient peaks)?
FTIR high Range @ 4% CO
Peaks significantly above NDIR Span (2K ppm)

## Slide 24: Hong Kong Coach - Data
At low concentrations
CO Follows same trend
FTIR Readings approximately
~50-75ppm lower

## Slide 25: Hong Kong Coach - Data

## Slide 26: Hong Kong Double Decker Bus - Data

## Slide 27: Hong Kong Double Decker Bus - Data
Unlike the previous test, CO data does not correlate
Peak in the beginning matches up well
Remainder of test, FTIR is constant DS shows a shift and deflections
Needs more analysis

## Slide 28: Hong Kong Double Decker Bus - Data
With FTIR, you can analyze many different variables – such as NH3 slip when exhaust temperature drops

## Slide 29: West Virginia University Test Cell
BOB-1000FT and Mexa 7200
All Mexa = diluted
FTIR Mixed sample points
(some raw, Some diluted)
Do not have adequate information yet to calculate Mass values for correlation

## Slide 30: Climbing Mount Fuji

## Slide 31: FTIR 25 Gas Graph

## Slide 32: Mount Fuji Cylinder Gas
Stable concentrations have been verified up to 3,200m (11,000 feet)
High Altitude Pressure Option
Maintains required Sample Cell Pressure, regardless of changing barometric pressure conditions.

## Slide 33: Conclusion
FTIR is a highly accurate (good correlation) method for exhaust gas measurement
There are a lot of advantages in using FTIR
FTIR has good correlation to conventional analyzers, for regulated components – while also measuring all gases of interest, with one analyzer
FTIR as a PEMS instrument will become increasingly important, as we continue to monitor and research additional gases

## Slide 34
Thank You !