## Slide 1: PEMS Conference 2014
Fuel Economy Data
Rick Walter, P.E.
HEM Data Corporation

## Slide 2
Heavy Duty
Fuel Economy & Consumption
Notes: What is going on here? Enhanced obd?

## Slide 3: J1939 HD Engine Parameters
  Engine speed, load (absolute & calculated)
  Vehicle speed
  Injector Flow Rate to engine
  Temperatures: coolant, ambient, catalyst
  Accelerator pedal and throttle position
  Diagnostic Trouble Codes (DTCs)
  Many, many parameters are available on J1939.

## Slide 4: Fuel Economy Easy to Get on HD Vehicles
Engine Fuel Rate – Resolution is 0.050 L/H
Engine Total Average Fuel Rate
Trip Average Fuel Rate
High Resolution Total Vehicle Distance – Resolutions is 0.005km
High Resolution Trip Distance
Engine Average Fuel Economy – Resolution is 0.0195 km/kg
Engine Instantaneous Fuel Economy
Engine Total Average Fuel Economy
Trip Drive Fuel Economy

## Slide 5: How Accurate is Fuel Data
NREL stated J1939 reports 6% better fuel economy than their lab testing on a conventional vehicle (UPS truck).
And J1939 reports 11% better fuel economy than lab testing on a hybrid vehicle.
Two approaches measured simultaneously
Reported highly consistent results.
SAE paper 2012-01-2049, Measured Laboratory & In- Use Fuel Economy… by M.P. Lammert, et al.

## Slide 6: How is Fuel Consumption Determined on J1939?
Both torque and fuel consumption are calculated not measured. Based on proprietary messages.
Fuel rate is based on Command-Fuel-Quantity. This is based on the Injector-Command to Fuel-Quantity- Calibration curve.
Verified with fuel-rail-pressure and fly-wheel feedback.
Torque is based on Command-Torque relative to the Torque-Curve for the engine. Related to engine speed, boost, altitude, temperature, etc. % Load is reported on J1939.

## Slide 7: Engine Torque on J1939
Notes: Question Demand Torque; other two are proportional

## Slide 8
Today’s Focus:
Light Duty
Fuel Economy & Consumption

## Slide 9: Sample OBD-II Parameters From LD Engine Controller
  Engine speed, load (absolute & calculated)
  Vehicle speed
  Temperatures: coolant, ambient, catalyst
  Accelerator pedal and throttle position
  Diagnostic Trouble Codes (DTCs)
  Mass Air Flow (MAF) Rate to engine
  Manifold Air Pressure (MAP)
  O2 sensor data, Lambda (A/F)
  Fuel trims (long and short term)

## Slide 10: Fuel Economy from Injectors
Fuel economy (miles/gal)
= 784.05 x VSS (KM/HR) / (Injector Volume (mL) / N)
x Eng. Speed (rev/min) x No of cylinders)
Where N = number of injections summed before reporting a value for a given cylinder, e.g. Toyota sums 10 pulses before transmitting.
Using EOBD fuel injector data. Update rate is typically 1-2/sec

## Slide 11: LD Injector Flow Rate
PID $5E in J1979 for OBD-II defines Injector Flow Rate – but seldom used.
Injector Flow Rate as part of EOBD data Some OEMs provide, but many do not.
Other key parameters are generally available with OBD-II as defined in J1979.
So how to calculate fuel consumption and fuel economy without injector flow rate?

## Slide 12
Fuel Economy Calculations
From MAF and A/F Ratio
Notes: Header?

## Slide 13: Fuel Economy
Most vehicles provide mass air flow (MAF) rate to calculate fuel consumption/economy
  Need: stoichiometric A/F ratio, vehicle speed, lambda, and fuel density
  Most commonly used, but Chrysler and some Honda vehicles don’t provide MAF.
If no injector data or MAF, then need to use MAP and ideal gas law. Helpful to model the engine. Least accurate.

## Slide 14: Fuel Economy from MAF
Fuel Economy (MPG)
= lambda x 6.807 x VS (KPH) / (MAF(g/s)
or = lambda x 11.00 x VS(MPH) / (MAF(g/s )
Use either average or instantaneous values.
Lambda is a ratio that defines the deviation from stoichiometric
6.17 - Density of gasoline (lb/gal) 0.62137km/mile
454 - Conversion (g/lb) 3600 - Conversion (sec/hr)
gal (fuel) = (gal/6.17lb x lb/454g) / 14.08(A/F) = 1/39,440.6 gal/g
39,440.6 / 3600 = 11.00 g-hr/gal-sec

## Slide 15: LD Engine Data

## Slide 16: Two Studies Presented
First study is on the presenter's 2010 Prius HEV
Second study is from an OEMs fleet of 111 LD vehicles.
Assumes 10% ethanol

## Slide 17: Fuel Economy MPG Calculations 2010 Prius HEV
Date | Miles | Fuel Tank | Injectors | MAF | Instr. Panel | % Difference (MAF to Inj) | % Difference (Instr to Inj)
25-Nov |  | - | 40.6 | 40.9 | 42.0 | 0.8% | 3.6%
2-Dec | 241.2 | - | 40.5 | 42.8 | 41.7 | 5.5% | 2.9%
10-Dec | 327.5 | 37.0 | 38.0 | 39.9 | 39.6 | 4.9% | 4.1%
20-Dec | 424 | 35.9 | 36.4 | 38.0 | 38.0 | 4.5% | 4.5%
13-Jan | 1260.4 | 40.1 | 40.1 | 42.9 | 42.8 | 7.2% | 6.9%
14-Mar | 239.1 | 34.8 | 35.1 | 37.0 | 37.1 | 5.3% | 5.6%
Summary | 2011.9 | 38.3 | 38.5 | 40.9 | 40.8 | 5.1% | 4.8%

## Slide 18: Conclusions from Prius Testing
Fuel injector data agrees well with fuel tank after 30 gal of fuel added
MAF based results show 5% higher fuel economy than fuel tank & injectors
MAF based data correlates with instrument panel display
So instrument cluster MPG is 5% high

## Slide 19: 2nd Test Study
Fleet from one OEM
Fuel Economy calculations were made as part of their study by HEM Data
Tested in several states IL, CA, MO, NY, GA, LA, OH, MD, OR, TX, MA
Sorted by engine model
Test period from 12/11 to 1/13 – so over a year

## Slide 20: Overview of 111 LD Vehicles

## Slide 21: Shows Excellent Correlation

## Slide 22: Correlation not as Good

## Slide 23: Some MAF Sensors Report 0 g/s some of the time

## Slide 24: Summary of Differences Fuel injector vs. MAF Based
Average = 2.8%
Std Dev = 5.1%
Mode = 1.2%
60 of the 111 vehicles were within +5%
32 of the 111 vehicles were within +3%
Summary chart % differences by model ranged from -5.2 to + 7.9%.

## Slide 25: Conclusions from Fleet Study
Using MAF and A/F ratio is valid alternative to calculating fuel consumption and fuel economy if injector data is not available.
MAF approach generally shows lower fuel consumption and higher fuel economy.
25 of 111 vehicles showed the opposite result.
Consistent results with hybrid vehicles as the first study shows.
Injector data and > 30 gal of gasoline refueling give excellent results.

## Slide 26: Conclusions from Fleet Study
Error could be 10% without noticing it on a single vehicle.
If injector data is not available, then to gain confidence compare MAF calculations to:
  Fuel tank additions of more than 30 gal, or
  Compare to a larger vehicle population
Could use this known difference to adjust the results to better match the injector results
Study is available at http://fuel.hemdata.com/

## Slide 27: PEMS Conference 2014
Fuel Economy Data
Rick Walter, P.E.
HEM Data Corporation
rickw@hemdata.com
248 559-5607 x111