## Slide 1
PEMS Testing to Assess Emissions
Implications of Electric Vehicles
Jeremy Johnson,
Josias Zietsman, Ph.D., P.E.
Reza Farzaneh, Ph.D., P.E.
Tara Ramani
Presented by
Yuche Chen, Ph.D.

## Slide 2: Objective: Accounting for Electric Vehicles in Air Quality Conformity
State-of-art practice assessment
  EV Market
  Emission and Energy Implication
  Implications for Air Quality and Conformity
Develop Texas-specific EV driving schedules
Develop Emission rates for EV
  Tailpipe emissions
  Emissions associated with electricity / charging
Develop EV Market Penetration Scenarios
Develop MOVES utility for emission estimation
Policy Implication and analysis

## Slide 3: Approach
A total of 12 vehicles were tested, including:
  4 HEVs (Camry, Fusion, Escape, Prius)
  4 PHEVs (Prius, three Volts)
  4 BEVs (Focus, three Leafs, Telsa??)
  Emissions
  Gaseous tailpipe emissions – HEV / PHEVs (charge sustaining mode, i.e. CS Mode)
  Source emissions - BEV / PHEVs (charge depletion mode, i.e. CD Mode)
    Calculated based on the EPA Power Profiler online tool and battery data from OBDII data loggers.
  Test Procedure
    Driving – One week for each vehicle at Environmental and Emissions Research Facility (EERF), College Station, TX
    Idling (Warm Start & Cold Start, Hot & Cool temperature) – Environmentally Controlled Test Chamber at EERF

## Slide 4: Test Protocol
In-use gaseous emissions - ECOSTAR system from Sensors Inc.
Each test included a GPS and an OBDII data logger to collect speed profile, battery profile (state of Charge, remaining battery power).
Pollutants: CO, CO2, NO, NO2, and THC

## Slide 5: Test Route
Consisted of both highway and city driving - repeated multiple times per vehicle
Total distance was ~31 miles.

## Slide 6: Vehicle Setup

## Slide 7: Test Results
Results were tabulated for each vehicle based on MOVES OpMode bins using the GPS/OBDII data for second-by second speed profile.
The data was then averaged for each MOVES OpMode bin, resulting in emissions rates for each vehicle in each OpMode bin.

## Slide 8: HEV-Running CO2 Emissions
Chart: Operating Mode Bins
| 0.0 | 1.0 | 11.0 | 12.0 | 13.0 | 14.0 | 15.0 | 16.0 | 21.0 | 22.0 | 23.0 | 24.0 | 25.0 | 27.0 | 28.0 | 29.0 | 30.0 | 33.0 | 35.0 | 37.0 | 38.0 | 39.0 | 40.0
2012 Camry | 0.36507 | 0.080126 | 0.41703 | 0.75386 | 1.7599 | 2.8592 | 4.1685 | 7.9997 | 0.70556 | 1.1199 | 1.7774 | 2.7399 | 3.7506 | 5.6244 | 8.4227 | 12.1982 | 15.8735 | 2.0773 | 4.0553 | 5.7421 | 7.5289 | 10.6706 | 16.4812
2012 Fusion | 0.28721 | 0.01557 | 0.31492 | 0.45385 | 0.90475 | 1.6009 | 1.8979 | 3.2138 | 1.1994 | 1.5959 | 2.3038 | 3.2619 | 4.8662 | 5.9894 | 7.5152 | 8.5847 | 11.6121 | 3.1729 | 4.4418 | 5.9566 | 7.364 | 10.0147 | 17.73
2012 Escape | 0.38649 | 0.0048177 | 0.24517 | 0.26093 | 1.3199 | 2.5292 | 3.8769 | 5.8952 | 1.0137 | 1.7528 | 2.566 | 3.6145 | 4.5857 | 6.1202 | 8.2273 | 9.9824 | 12.3061 | 4.6174 | 6.634 | 8.722 | 10.389 | 12.6659 | 16.618
2011 Prius | 0.1227 | 0.001792 | 0.03526 | 0.14799 | 1.1137 | 2.4688 | 4.0622 | 7.0455 | 0.48125 | 0.91989 | 1.825 | 2.887 | 3.6907 | 5.8191 | 8.3982 | 10.7506 | 12.0656 | 2.3116 | 4.1587 | 6.5251 | 8.5168 | 11.4935 | 15.3488

## Slide 9: HEV-Running NOx Emissions
Chart: Operating Mode Bins
| 0.0 | 1.0 | 11.0 | 12.0 | 13.0 | 14.0 | 15.0 | 16.0 | 21.0 | 22.0 | 23.0 | 24.0 | 25.0 | 27.0 | 28.0 | 29.0 | 30.0 | 33.0 | 35.0 | 37.0 | 38.0 | 39.0 | 40.0
2012 Camry | 7.8159e-06 | 8.9286e-07 | 1.6081e-05 | 9.5506e-06 | 1.6316e-05 | 3.7553e-05 | 6.3151e-05 | 0.00016157 | 1.3778e-06 | 5.4184e-05 | 9.0176e-05 | 0.00014127 | 7.5531e-05 | 1.1239e-05 | 2.9829e-05 | 5.4247e-05 | 0.0001514 | 1.6344e-05 | 5.0051e-05 | 5.0633e-05 | 6.9077e-05 | 0.00027717 | 0.00031541
2012 Fusion | 1.5346e-05 | 3.6383e-07 | 1.2959e-05 | 9.2617e-06 | 2.4706e-05 | 2.8105e-05 | 0.00010864 | 0.00019028 | 4.678e-05 | 2.8241e-05 | 4.3061e-05 | 4.5192e-05 | 0.00014203 | 7.2816e-05 | 0.00014424 | 0.00025091 | 0.00021149 | 3.1429e-05 | 2.7413e-05 | 3.4532e-05 | 5.8252e-05 | 8.6316e-05 | 0.00026172
2012 Escape | 3.029e-05 | 1.4151e-07 | 9.6335e-06 | 9.9688e-06 | 0.00011419 | 0.00010047 | 0.0001907 | 0.00056198 | 0.00011547 | 0.00011961 | 0.00014248 | 0.00016412 | 0.00026 | 0.000455 | 0.00081008 | 0.0011904 | 0.0029012 | 0.00039529 | 0.0005965 | 0.001153 | 0.002919 | 0.0031526 | 0.0067545
2011 Prius | 3.2995e-06 | 0 | 8.7912e-07 | 7.8125e-06 | 1.8358e-05 | 1.7292e-05 | 1.9583e-05 | 3.6355e-05 | 8.9706e-06 | 2.02e-05 | 1.5696e-05 | 2.881e-05 | 0.0001544 | 6.9158e-05 | 0.00010833 | 0.000268 | 0.00019482 | 2.75e-05 | 3.7226e-05 | 0.00025918 | 0.0004162 | 0.00029722 | 0.0064321

## Slide 10: HEV-Idling NOx Emissions
Chart: Test Condition
| Hot Test (Cold Start) | Hot Test | Cold Test (Cold Start) | Cold Test
2012 Camry | 0.041497 | 0.19431 | 0.018611 | 0.0022417
2012 Fusion | 0.19099 | 0.017791 | 0.025664 | 0.0057099
2012 Escape | 0.22393 | 0.01131 | 0.12859 | 0.00777
2011 Prius | 0.092818 | 0.00039 | 0.034008 | 0.02638

## Slide 11: PHEV CS Mode CO2 Emissions
Chart: Operating Mode Bins
| 0.0 | 1.0 | 11.0 | 12.0 | 13.0 | 14.0 | 15.0 | 16.0 | 21.0 | 22.0 | 23.0 | 24.0 | 25.0 | 27.0 | 28.0 | 29.0 | 30.0 | 33.0 | 35.0 | 37.0 | 38.0 | 39.0 | 40.0
2012 Prius Plug-In | 0.20678 | 0.0004633 | 0.05139 | 0.12873 | 0.53204 | 1.3154 | 1.6476 | 4.5797 | 0.58496 | 0.70182 | 1.2096 | 1.9932 | 3.3508 | 5.1578 | 7.4823 | 8.9056 | 10.4998 | 2.0203 | 3.1978 | 4.7274 | 5.74 | 7.4073 | 13.2559
2012 Volt #1 | 1.3334 | 0 | 0.56323 | 0.39948 | 0.36318 | 0.21302 | 0.0097783 | 0.41095 | 3.7029 | 3.6816 | 3.6032 | 3.6639 | 2.8625 | 3.0685 | 3.3811 | 2.3718 | 3.5162 | 5.1218 | 5.6766 | 5.7992 | 6.3075 | 7.0044 | 8.866
2012 Volt #2 | 1.2726 | 0.0026036 | 0.79837 | 0.26389 | 0.24694 | 0.1378 | 0.33944 | 0.4876 | 3.9546 | 4.2525 | 4.3251 | 4.2038 | 3.5425 | 3.0156 | 4.2726 | 2.6003 | 3.6291 | 4.9953 | 6.0334 | 6.9239 | 7.8875 | 8.0261 | 8.5809
2011 Volt | 1.4825 | 0.0057356 | 0.64922 | 0.28164 | 0.78408 | 0.94339 | 0.87062 | 2.0955 | 3.7326 | 4.0771 | 4.4629 | 4.7617 | 4.6094 | 4.2374 | 5.7533 | 6.2495 | 8.3094 | 4.8351 | 6.2797 | 7.4718 | 7.9544 | 8.5186 | 8.9883

## Slide 12: PHEV CS Mode NOx Emissions
Chart: Operating Mode Bins
| 0.0 | 1.0 | 11.0 | 12.0 | 13.0 | 14.0 | 15.0 | 16.0 | 21.0 | 22.0 | 23.0 | 24.0 | 25.0 | 27.0 | 28.0 | 29.0 | 30.0 | 33.0 | 35.0 | 37.0 | 38.0 | 39.0 | 40.0
2012 Prius Plug-In | 1.0889e-05 | 0 | 1.6667e-07 | 5.7143e-06 | 1.9275e-05 | 3.381e-05 | 7.3947e-05 | 0.00069339 | 1.3306e-05 | 3.1522e-05 | 1.8267e-05 | 1.6771e-05 | 9.3067e-05 | 0.00022207 | 0.00020803 | 0.000504 | 0.0018311 | 7.5279e-05 | 3.0168e-05 | 7.6341e-05 | 0.00011896 | 6.7813e-05 | 0.0029747
2012 Volt #1 | 1.109e-05 | 0 | 2.5641e-06 | 1.9863e-06 | 1.7094e-06 | 6.5789e-07 | 2.1739e-07 | 6.2887e-06 | 5.0925e-05 | 2.7429e-05 | 2.7217e-05 | 2.5734e-05 | 2.9111e-05 | 4.4048e-05 | 3.4727e-05 | 3.9722e-05 | 0.0003868 | 2.363e-05 | 1.4815e-05 | 1.6e-05 | 1.0748e-05 | 9.5e-06 | 8.7385e-05
2012 Volt #2 | 0.00015084 | 3.3654e-07 | 2.59e-05 | 2.68e-05 | 2.0074e-05 | 7.1542e-06 | 1.0804e-05 | 3.467e-05 | 0.00026859 | 0.00012969 | 0.00019952 | 0.00014533 | 0.00012649 | 0.00036496 | 0.0004206 | 0.00051462 | 0.00065523 | 0.00021992 | 0.00020182 | 0.00027962 | 0.00041031 | 0.00031377 | 0.00051918
2011 Volt | 9.8713e-05 | 2.8944e-07 | 3.7908e-05 | 4.5733e-05 | 3.7953e-05 | 0.00016879 | 9.457e-05 | 0.00029308 | 0.00019011 | 0.00020878 | 0.00020761 | 0.00023696 | 0.00021646 | 0.0002066 | 0.00060741 | 0.00098102 | 0.0010544 | 0.00023045 | 0.00028118 | 0.0003735 | 0.00042355 | 0.00043121 | 0.00045054

## Slide 13: PHEV CD Mode Power Consumption
Chart: Operating Mode Bins
| 0.0 | 1.0 | 11.0 | 12.0 | 13.0 | 14.0 | 15.0 | 16.0 | 21.0 | 22.0 | 23.0 | 24.0 | 25.0 | 27.0 | 28.0 | 29.0 | 30.0 | 33.0 | 35.0 | 37.0 | 38.0 | 39.0 | 40.0
2012 Prius Plug-In | -0.0061241 | -0.00099989 | -0.00050294 | 0.0058925 | 0.0025065 | 0.0061708 | 0.0081246 | 0.014848 | -0.00012658 | 0.0011923 | 0.0030033 | 0.0064148 | 0.009397 | 0.015131 | 0.0183 | 0.0041354 | 0.0075753 | 0.011144
2012 Volt #1 | -0.0028477 | 0.00038749 | -1.5993e-05 | 0.00076784 | 0.0029164 | 0.004216 | 0.0043987 | 0.010441 | -0.00013109 | 0.0014107 | 0.0026328 | 0.0037604 | 0.0054066 | 0.0080095 | 0.012266 | 0.016352 | 0.026611 | 0.0024356 | 0.0055804 | 0.0082099 | 0.011279 | 0.013207 | 0.027728
2012 Volt #2 | -0.0049404 | 0.00029133 | -0.00096352 | 0.0014345 | 0.0039855 | 0.0060502 | 0.0076891 | 0.014138 | -0.0016723 | 0.0014219 | 0.0028917 | 0.0047269 | 0.0074258 | 0.0095646 | 0.016542 | 0.021783 | 0.029266 | 0.0010294 | 0.0060162 | 0.0084373 | 0.01226 | 0.018364 | 0.029557
2011 Volt | -0.004274 | 0.00040414 | -0.00043602 | 0.002006 | 0.0054133 | 0.0071571 | 0.0091748 | 0.015584 | -0.0023643 | 0.0012763 | 0.003032 | 0.0044205 | 0.0073149 | 0.010164 | 0.014094 | 0.020891 | 0.028739 | 0.0012858 | 0.0061231 | 0.0094007 | 0.012794 | 0.02168 | 0.031663
Notes: The Prius had no CD mode data in the higher speed/acc bins

## Slide 14: PHEV CS Mode Idling NOx Emissions
Chart: Test Condition
| Hot Test (Cold Start) | Hot Test | Cold Test (Cold Start) | Cold Test
2012 Prius Plug-In | 0.0018667 | 0.00404 | 0 | 0
2012 Volt #1 | 0.0045268 | 0.0015498 | 0.060001 | 0
2012 Volt #2 | 0.12898 | 0.098122 | 0.0094772 | 0
2011 Volt | 0.12749 | 0.023907 | 0.12693 | 0.015211

## Slide 15: PHEV CD Mode Idling NOx Emissions
Chart: Test Condition
| Hot Test (Cold Start) | Hot Test | Cold Test (Cold Start) | Cold Test
2012 Prius Plug-In | 0.60357 | 0.24915
2012 Volt #1 | 0.22561 | 0.25363 | 0.64762 | 0.66547
2012 Volt #2 | 0.47682 | 0.32332 | 1.5448 | 0.60092
2011 Volt | 0.60745 | 0.44089 | 1.5219 | 0.94384

## Slide 16: BEV Power Consumption
Chart: Operating Mode Bins
| 0.0 | 1.0 | 11.0 | 12.0 | 13.0 | 14.0 | 15.0 | 16.0 | 21.0 | 22.0 | 23.0 | 24.0 | 25.0 | 27.0 | 28.0 | 29.0 | 30.0 | 33.0 | 35.0 | 37.0 | 38.0 | 39.0 | 40.0
2011 Leaf 1 | 0.0011364 | 0.00039241 | 0.0011834 | 0.0004717 | 0.0018519 | 0.0010274 | 0.0021505 | 0.0065957 | 0.0011719 | 0.0023697 | 0.0032839 | 0.0042461 | 0.00727 | 0.0098077 | 0.0085714 | 0.018519 | 0.020062 | 0.0046779 | 0.0075835 | 0.0092078 | 0.012255 | 0.017969 | 0.019444
2011 Leaf 2 | 0.001504 | 0 | 0.002 | 0.0018797 | 0.0027778 | 0.0053191 | 0.0034247 | 0.0084375 | 0.00054545 | 0.0014315 | 0.0030327 | 0.0041076 | 0.0069231 | 0.0081461 | 0.02378 | 0.018966 | 0.023723 | 0.0033019 | 0.0067738 | 0.010904 | 0.014898 | 0.013736 | 0.028516
2011 Leaf 3 | 0.00085094 | 7.4184e-05 | 0.0016043 | 0.0015306 | 0.0018919 | 0.004878 | 0.00056818 | 0.0087302 | 0.0013433 | 0.00096525 | 0.0032702 | 0.0034916 | 0.0057339 | 0.0073394 | 0.013918 | 0.026316 | 0.019048 | 0.0043624 | 0.0060313 | 0.0094872 | 0.012216 | 0.013415 | 0.025
2013 Focus | -0.0043658 | 0.00023095 | 1.8072e-05 | 0.00089671 | 0.0015677 | 0.0030656 | 0.00354 | 0.0052244 | 0.0011043 | 0.0016614 | 0.0025963 | 0.0040356 | 0.0057976 | 0.0081257 | 0.012792 | 0.013575 | 0.01948 | 0.0039093 | 0.0059141 | 0.0081624 | 0.010389 | 0.013539 | 0.023547

## Slide 17: BEV Idling NOx Emissions
Chart: Test Condition
| Hot Test (Cold Start) | Hot Test | Cold Test (Cold Start) | Cold Test
2011 Leaf 1 | 0.35925 | 0.42456 | 1.9269 | 0.86872
2011 Leaf 2 | 0.91444 | 0.42456 | 1.9595 | 0.71849
2011 Leaf 3 | 0.75115 | 0.62051 | 1.7636 | 0.60745
2013 Focus | 0.34945 | 0.34618 | 0.32332 | 0.17309

## Slide 18: Conclusions
Completed the testing of electric vehicles
Results will be used for emission estimation with uncertainties in EV market penetration, power generation emission, and energy policies.
Determine overall emission impacts / health impacts of EVs

## Slide 19: Contact
Yuche Chen
Texas A&M Transportation Institute
Email: y-chen@tti.tamu.edu
979-862-2232

## Slide 20: Supplemental Test Results

## Slide 21: Test Results – HEV CO Emissions
Chart: Operating Mode Bins
| 0.0 | 1.0 | 11.0 | 12.0 | 13.0 | 14.0 | 15.0 | 16.0 | 21.0 | 22.0 | 23.0 | 24.0 | 25.0 | 27.0 | 28.0 | 29.0 | 30.0 | 33.0 | 35.0 | 37.0 | 38.0 | 39.0 | 40.0
2012 Camry | 0.009156 | 0.00037487 | 0.00034041 | 0.0016411 | 0.016132 | 0.055057 | 0.12393 | 0.24543 | 0.026296 | 0.018921 | 0.023031 | 0.020597 | 0.025806 | 0.066277 | 0.1957 | 0.35544 | 1.8278 | 0.031614 | 0.011642 | 0.024431 | 0.1084 | 0.54774 | 4.0769
2012 Fusion | 0.017772 | 0.00011955 | 0.0024863 | 0.001041 | 0.0028273 | 0.0056627 | 0.0069873 | 0.016518 | 0.015934 | 0.014573 | 0.017184 | 0.016504 | 0.07501 | 0.046277 | 0.072169 | 0.11002 | 0.78617 | 0.15804 | 0.062639 | 0.063174 | 0.38816 | 1.904 | 5.4925
2012 Escape | 0.019121 | 6.4016e-07 | 0.0010581 | 0.0012541 | 0.0041621 | 0.01074 | 0.012363 | 0.027682 | 0.017722 | 0.0089997 | 0.013188 | 0.01417 | 0.014434 | 0.028757 | 0.072353 | 0.084791 | 0.36957 | 0.17083 | 0.14224 | 0.23042 | 0.58355 | 1.602 | 3.8441
2011 Prius | 0.0003068 | 6.0259e-06 | 2.5824e-05 | 0.00030177 | 0.0019055 | 0.0054923 | 0.012777 | 0.013199 | 0.00040718 | 0.000889 | 0.0019536 | 0.0034274 | 0.005883 | 0.0080902 | 0.0089673 | 0.016084 | 0.013556 | 0.0014032 | 0.002966 | 0.0049047 | 0.0065652 | 0.0048922 | 0.0102

## Slide 22: Test Results – HEV THC Emissions
Chart: Operating Mode Bins
| 0.0 | 1.0 | 11.0 | 12.0 | 13.0 | 14.0 | 15.0 | 16.0 | 21.0 | 22.0 | 23.0 | 24.0 | 25.0 | 27.0 | 28.0 | 29.0 | 30.0 | 33.0 | 35.0 | 37.0 | 38.0 | 39.0 | 40.0
2012 Camry | 2.4399e-05 | 1.631e-06 | 1.5263e-05 | 2.9375e-05 | 4.2581e-05 | 7.9595e-05 | 0.00012811 | 0.0002776 | 9.4062e-05 | 8.6508e-05 | 6.4816e-05 | 6.556e-05 | 0.00014455 | 0.00027605 | 0.00092595 | 0.00064114 | 0.0047042 | 0.00010802 | 0.00010749 | 0.00016293 | 0.00031083 | 0.00093385 | 0.012448
2012 Fusion | 3.4226e-05 | 1.4553e-07 | 2.7551e-06 | 2.0805e-06 | 5.9804e-06 | 1.9583e-05 | 3.55e-05 | 9.8128e-05 | 2.4669e-05 | 1.0666e-05 | 2.0493e-05 | 1.3805e-05 | 0.00012608 | 5.569e-05 | 0.00028577 | 0.00037295 | 0.0011181 | 0.00036817 | 0.00016439 | 0.00015616 | 0.00077971 | 0.0039632 | 0.012022
2012 Escape | 0.0001598 | 1.0782e-07 | 1.3351e-05 | 1.838e-05 | 2.2426e-05 | 3.3458e-05 | 5.1e-05 | 0.00014818 | 4.3674e-05 | 2.6858e-05 | 3.5035e-05 | 3.6016e-05 | 6.3216e-05 | 0.0001 | 0.00022677 | 0.000346 | 0.00061172 | 0.0015315 | 0.00075517 | 0.00060134 | 0.0021583 | 0.0057832 | 0.013972
2011 Prius | 5.956e-06 | 3.5377e-08 | 0 | 2.0833e-06 | 1.7164e-05 | 6.3125e-05 | 0.00032271 | 0.00022589 | 1.4912e-05 | 2.61e-05 | 4.5599e-05 | 0.00010333 | 0.0001695 | 0.00028105 | 0.00017182 | 0.00040686 | 0.00048071 | 2.2148e-05 | 5.0663e-05 | 0.00016194 | 0.00034815 | 0.00025333 | 0.0010116

## Slide 23: Test Results – PHEV CS Mode CO Emissions
Chart: Operating Mode Bins
| 0.0 | 1.0 | 11.0 | 12.0 | 13.0 | 14.0 | 15.0 | 16.0 | 21.0 | 22.0 | 23.0 | 24.0 | 25.0 | 27.0 | 28.0 | 29.0 | 30.0 | 33.0 | 35.0 | 37.0 | 38.0 | 39.0 | 40.0
2012 Prius Plug-In | 0.00031731 | 3.1086e-06 | 0.00013117 | 0.00027488 | 0.00051275 | 0.00087952 | 0.0011561 | 0.0061895 | 0.00036614 | 0.00030696 | 0.00066129 | 0.0011311 | 0.0011013 | 0.0035618 | 0.0063728 | 0.0085673 | 0.0063617 | 0.00081595 | 0.0013343 | 0.0027001 | 0.0041734 | 0.0031156 | 0.0047934
2012 Volt #1 | 0.063584 | 0 | 0.0014521 | 0.0027498 | 0.0043034 | 0.001293 | 0.0035848 | 0.012915 | 0.12359 | 0.09188 | 0.1164 | 0.075597 | 0.024308 | 0.021143 | 0.10382 | 0.042188 | 0.18977 | 0.28073 | 0.28725 | 0.30805 | 0.47349 | 0.74739 | 1.0361
2012 Volt #2 | 0.04644 | 7.8059e-06 | 0.0016083 | 0.00050109 | 0.00042881 | 0.00018557 | 0.00049603 | 0.0015571 | 0.025677 | 0.013095 | 0.015739 | 0.01115 | 0.012157 | 0.015407 | 0.035974 | 0.018251 | 0.03963 | 0.12461 | 0.10679 | 0.21464 | 0.34886 | 0.7632 | 0.98023
2011 Volt | 0.070734 | 8.2706e-05 | 0.0024721 | 0.0015656 | 0.0029039 | 0.0031188 | 0.0049184 | 0.006303 | 0.062198 | 0.065597 | 0.062491 | 0.074826 | 0.034323 | 0.028796 | 0.032176 | 0.12969 | 0.11337 | 0.15477 | 0.13571 | 0.25925 | 0.3387 | 0.48554 | 0.83981

## Slide 24: Test Results – PHEV CS Mode THC Emissions
Chart: Operating Mode Bins
| 0.0 | 1.0 | 11.0 | 12.0 | 13.0 | 14.0 | 15.0 | 16.0 | 21.0 | 22.0 | 23.0 | 24.0 | 25.0 | 27.0 | 28.0 | 29.0 | 30.0 | 33.0 | 35.0 | 37.0 | 38.0 | 39.0 | 40.0
2012 Prius Plug-In | 7.9812e-06 | 1.2484e-08 | 0 | 1.8987e-06 | 5.6e-06 | 8.8095e-06 | 3.871e-06 | 6.6847e-05 | 2.8909e-06 | 6.9605e-06 | 5.5135e-06 | 6.1905e-06 | 3.4444e-05 | 2.8947e-05 | 5.193e-05 | 0.0001214 | 0.00027406 | 4.8912e-05 | 4.1278e-05 | 5.8375e-05 | 6.7399e-05 | 9.913e-05 | 0.00046813
2012 Volt #1 | 0.0006556 | 0 | 0.00091829 | 0.0010299 | 0.0012957 | 0.00061316 | 6.5217e-07 | 0.00041629 | 0.00034313 | 0.00096167 | 0.00057033 | 0.00037252 | 0.00017889 | 0.00026869 | 0.00068945 | 0.0001575 | 0.0026926 | 0.00086124 | 0.0011526 | 0.001524 | 0.0020332 | 0.0035855 | 0.0044614
2012 Volt #2 | 0.0005533 | 4.7247e-06 | 7.3556e-05 | 0.00018741 | 0.00038108 | 6.6403e-05 | 2.3214e-06 | 3.5714e-06 | 0.00072731 | 8.8755e-05 | 0.00020728 | 0.00025442 | 0.00086049 | 0.0011038 | 2.36e-05 | 0.00011577 | 0.00071415 | 0.00016972 | 0.0002732 | 0.0015438 | 0.0022052 | 0.0009883 | 0.0017165
2011 Volt | 0.0002511 | 4.3367e-06 | 0.00014218 | 0.0001693 | 0.00015637 | 0.00016621 | 9.7527e-05 | 0.00019919 | 7.887e-05 | 6.9769e-05 | 7.8132e-05 | 9.7042e-05 | 0.0001096 | 9.8924e-05 | 0.00011756 | 0.00015776 | 0.00017539 | 0.00022757 | 0.0003178 | 0.00080012 | 0.0010307 | 0.00067983 | 0.00068396