## Slide 1: On-Going Challenges for Off-Road/Nonroad Pilot In-Use Emissions Testing
2013 PEMS Conference and Workshop, Ce-Cert
April 11, 2013
John Bowman – Cummins Inc.

## Slide 2: Content
Review of several Tier 4 applications tested summer of 2012
  Installation overview and test observations
    Front Loader
    Excavator
    Mobile Air Compressor
Summary of top Challenges
Going Forward
Q&A

## Slide 3: Wheel Loader Test
8.9L Tier 4 HDOH HDIUT test protocols including customer operated
Max Ambient Temp 98.6 deg F
Possibility of Rain

## Slide 4: Wheel Loader PEMS Installation
Environment case used (chance of rain and better vibration isolation at the expense of greater heat retention on gaseous analyzer)
Honda 2k invertor generator for power
Ratchet straps for retention generator and environmental case
Specialized suction cups hold exhaust flow meter
No PM measurement for this test

## Slide 5: Front Loader Test Observations
Very limited on installation space
  PM measurement equipment was not possible unless equipment placed on Roll Over Protection
Duty Cycle not conducive to HDOH or WBW PEMS testing protocols
  No NTE events observed over 4.7 hours of non-idle operation
  Was not able to retain %50 of averaging windows at %15 minimum power threshold for Work Based Window methods

## Slide 6: Excavator Test
6.7L Tier 4
HDOH HDIUT test protocols including customer operated
Maximum Ambient Temp 91.4 deg F
No rain in forecast

## Slide 7: Excavator PEMS Installation Detail
Gaseous emissions only using SEMTECH-DS w/ EFMII
Testing preparation followed our on road process with respect to installation practices.
  No special frames or mounts were fabricated.
  Sensors vibration plate, ratchet straps, plastic strap ties, and suction cups
Honda 2k invertor generator for power

## Slide 8: Excavator Test Observations
Excessive Vibration
  Panels came loose on SEMTECH
  Diffuser on weather probe came apart
  Issues with data recorder (lost 80 minutes of data requiring a restart) are suspected to be vibration related
Lack of mounting locations
  PM measurement equipment would be very difficult with most equipment configurations likely requiring custom frame mounts to be fabricated
  Few options to relocate away from heat rejection
Good duty cycle for emissions testing
  Suitable for NTE testing with 109 NTE events over 5+ hours of non-idle operation
  Work Based Window analysis meets 20% minimum average power threshold

## Slide 9: Air Compressor Test
8.9L Tier 4
Simulated Operation
  Not customer operated
PEMS equipment kept in test trailer

## Slide 10: Air Compressor Test Observations
Stationary application easy to PEMS test
  Can keep equipment off to the side and easily keep the equipment protected from the conditions the mobile machine subject the equipment to
Relatively constant speed and load gives no issue to producing NTE events or high average power averaging windows for WBW methods
Duty Cycle presents some unique challenges
  The machine always operates in NTE zone
  Protocols currently do not allow equipment to start and auto zero if currently in an NTE. This will not allow equipment to zero and excessive drift was observed after 2+ hours of operation. Engine was stopped to allow a zero and restarted
  Batch sampling devices may
  Current protocols are such that one long NTE event would be limited by the 600 second NTE limit and thus only one NTE event would be evaluated over this
  After manually time-aligning data, EMROAD shifted the data again during it’s time alignment by 77 seconds. Constant RPM applications may cause these issues with the EMROAD analysis tool.

## Slide 11: Summary of top Challenges
Application Diversity
  Each application requires very specific installation requirements that may require customer rigging or frame work to appropriately constrain PEMS
  Will require significantly increased pre-screening to be successful in procuring equipment that can be fully equipped with Gaseous and PM PEMS while also meeting necessary duty cycle requirements
Pre-fabricated frame
Installation by JCR

## Slide 12: Summary of top Challenges (continued)
  Working in customer operations much more difficult than HDOH applications in many situations
Environmental concerns
  Vibration exposure continues to be a challenge
  Extreme ambient temperatures especially at the hot end of the spectrum
    Almost none of the applications have conditioned cab space available unlike on-road applications
    Equipment space is very limited and may not be able to avoid engine waste heat rejection
    Equipment starts exhibiting performance issues at approximately 100 Deg F
  Dusty Conditions

## Slide 13: Going Forward…
Rigorous pre-screening
  Checking for installation feasibility and any necessary fabrication
  Potentially monitor duty cycle
Improved vibration isolation
Smaller PEMS footprint
Supply environmental cases or cloth covers (tent) with ducted, filtered cooling air
    Inlet air can be cyclone filtered for dust and drawn at locations away from excessive heat rejection from engine

## Slide 14: Questions?