## Slide 1: Compliance Testing Applications: Installation Safety / Data Processing Tools
CeCERT 2013 PEMS Conference & Workshop
April 11, 2013
Steven S. Trevitz
Sr. Staff Engineer
Volvo Group Trucks Technology

## Slide 2: Industry Developments (How Do PEMS Help Development and Compliance)
The Vehicle is a PEMS
  Electronic Contols sensors, models
  OBD legal requirement
Data Collection ECM
  Service Tools
  Engineering Tools
    Development
    Logging
Compliance-grade §1065 PEMS
  Not used for development
    Resource intensive
    Different data of interest

## Slide 3: Product Development / Validation
Testing of Vehicle / Engine / EATS
  Local
  Expedition
  Customer Field
Data Acquisition
  ECM + Instrumentation
    CSM UniCAN
    Sensors
    Lab Equipment
      AVL Micro Soot Sensor engine-out soot

## Slide 4: Compliance Test Equipment
Gas PEMS: Horiba OBS-2200
      NOx, HC, CO, CO2
      Exhaust Flow
      Ambient Temp, Humidity, and Pressure
PM PEMS: AVL 494
      Real-Time Soot
      Gravimetric Filter Module
Central Controller: CSM UniCAN
      ECM Data
      Gas & PM PEMS synchronization
      O2
      GPS
      EATS-out Exhaust Temp

## Slide 5: Volvo-Designed Subsystems & Integration 18-hour unattended operation
Installation
  In-Cab
  Frame-side mount
  Back-of-Cab to become primary installation method
Gassing System
  Air, Quad-blend, FID fuel
  Hourly zero and span calibrations
Power
  Diesel generator
  Alternator + inverters
Software
  Analysis, Alignment, Computation, Reporting, and Validation

## Slide 8: Generator Safety
Mounting DOT-legal
  Secure
  Fuel tank
Electrical
  Grounding
    Shore Power
  Short-Circuit Prevention and Protection
Exhaust
Heat
  Vehicle, Solar, Pavement
Safety Shutdown System

## Slide 9: Synchronization and Control
PM PEMS requires [HC], exhaust flow, & exhaust temp from Gas PEMS
Gas PEMS undergoes hourly calibrations
UniCAN detects Gas PEMS calibration:
  Signals PM PEMS to suspend filter loading during Gas PEMS calibration
  PM PEMS filter loading will be terminated if FID extinguishes
  Result Consistent hourly trigger for all 3 data loggers
Gas PEMS
Uni-CAN
PM PEMS
Zero on/off
FID on/off
Span on/off
Filter on/off
Filter on/off
Control
State

## Slide 10: Data Management and Processing
All data logging at 10 Hz
3 systems combined generate 85 MB/hour of data
  Typical test of 12 hours > 1 GB of data, 26 files
Specialized software
  View data
  Concatenation and continuity
  Alignment and time correction
  Gaseous and PM Mass calculations
  Parse to 1 Hz
  NTE calculations
  Report preparation Engineering Analysis, Validation, EPA/CARB submissions

## Slide 11: Graphical Viewer – Rapid Post Test Check

## Slide 12: 10 Hz Time Synchronization
UniCAN logs the time of record Continuous, Real-Time Operation
Clock time for Gas PEMS and PM PEMS are equalized at 1st hourly calibration (triggered by leading edge of Gas PEMS zero gas “ON”)
At subsequent hourly calibrations, the clock time gain/loss of Gas PEMS and PM PEMS is corrected by deleting or adding the appropriate time
  Data row adjustment
  Adjusted by 0.1 second increments
  Adjustments < 1 second well within accepted alignment error
  Correction applied to calibration period no emissions data logged
Result Coarse consistent alignment of all channels from all data loggers

## Slide 13: 10 Hz Alignment
Graphical alignment software allows visual expansion of 10 Hz data
  Waveforms are aligned by superimposition and quickly checked from test beginning to end
Gaseous concentration data is inherently aligned by OBS procedure
  Important feature as only CO2 has well-defined waveform on EATS-equipped, modern engine emissions
Exhaust flow is aligned to CO2 concentration.
  Critical for mass calculations
ECM modeled exhaust flow is aligned to OBS measured exhaust flow
PM PEMS has an established lag from sample zone to detector
  Empirical data necessary to establish alignment
  Often, the soot concentration waveform lacks definition

## Slide 14: Process NTE & Report 1Hz Data

## Slide 15: Validation
Real-time waveforms
  NOx sensor vs analyzer
  Exhaust flow ECM vs PEMS
  Fuel CO2 vs PEMS
  O2 sensor vs chemical balance
NTE calculation
  BSCO2
    Fuel Carbon Balance
    Thermal Efficiency, expected value

## Slide 16: Questions, Comments, Discussion