## Slide 1
Particle Sensor Performance & Durability for OBD Applications & Beyond
Imad Khalek* & Vinay Premnath , SwRI
CE-CERT Workshop, April 11, 2013
Ikhalek@swri.org

## Slide 2: SwRI®

## Slide 3: Acknowledgments
This work is funded by PSPD consortium members:

## Slide 4: Brief
This work was developed in Year 1 of SwRI Particle Sensor & Durability (PSPD) Consortium
  The focus of Year 1 was on performance
  The focus of the upcoming Year 2 is on Performance & Durability

## Slide 5: Particle Sensor Applications
Onboard vehicles downstream of exhaust particle filters for:
  OBD Requirement (highway vehicles, potentially nonroad)
  Filter leak detection and durability
    QA/QC
    In-use screening
  Onboard vehicles engine out
    Active particle emissions control
    Engine mapping (Real World)
    EGR cooler diagnostics through particle dynamics
Retrofit Applications
In-Use PEMS Testing (Very Simple System)
  Can be applied to very difficult applications (e.g. nonroad)
Smoke meter replacement (laboratory use)
Replacement of expensive laboratory instruments

## Slide 6: Objectives
To investigate exhaust particle sensor performance and durability using diesel engine platform
  Compare sensor performance with that of laboratory particle instruments under different engine operating conditions:
    Concentration, composition, temperature, velocity, pressure, etc…
  Determine short and mid term (few days) variability using multiple sensors
To determine sensor short term survivability under:
    DPF regeneration
    Increased backpressure
    Cold temperature environment
To determine long term durability under various engine operating conditions

## Slide 7: Engine Test Cell Setup

## Slide 8: Engine Test Cell Setup

## Slide 9: Particle Instruments
TSI EEPS (Size, Number, Charge
AVL MSS (Soot Mass)
SwRI SPSS, Facilitate Solid Particle Measurement
(Used Upstream of EEPS)
Pegasor PPS
Real Time Soot Mass

## Slide 10: Electricfil Cumulative Sensor
Particles collect on an electrode with high electric resistor
Electric resistance decrease with soot loading
As resistance reaches a threshold, sensor is regenerated, and the process starts again
Change in resistance over time is determined between:
  End of Regeneration and Beginning of Regeneration
This sensor provides integrated soot accumulation on the sensor surface over a period of time:
  Time will be short if the concentration is high
  Time will be long if the concentration is low
  For an engine producing ~0.03 g/hp-hr, four regeneration events took place in 20 minutes
Even if the sensor is very accurate, particle deposition will have to be proportional to engine exhaust to get a proper weighting to exhaust emissions, especially under transient operation (a very challenging fluid dynamic problem)

## Slide 11: Emisense Real Time Sensor
A sample of exhaust is extracted into the sensor electrode region by a venturi using exhaust velocity
Naturally charged particles are captured between two electrodes in a electric field
Captured particles break away from the surface of the electrode due to high charge buildup
Electrometer current is an output associated with particle deposition and release from the electrode surface.
  Better understanding of sensor fundamental performance is currently being developed by the sensor manufacturer

## Slide 12: NGK-NTK Real Time Sensor
Air driven by an external pump is ionized via a positive corona needle to charge the particles
The high velocity ionized air creates a low pressure region where exhaust enters and mixes with it.
The excess ions are trapped
The positively charged particles enter and escape a Faraday cup creating a net total charge that is proportional to particle concentration
No trapping of particles is required for this method to work

## Slide 13: Sensor Experiments Test Matrix
 | Nominal Sample Zone Temperature of 500 oC |  |  |  | 
Nominal Velocity, m/sec | 10 | 30 | 50 |  | 
 | Nominal Sample Zone Temperature of 390 oC to 440oC |  |  |  | 
Nominal Velocity, m/sec | 10 | 30 | 50 | 70 | 90
 | Nominal Sample Zone Temperature of 300 oC |  |  |  | 
Nominal Velocity, m/sec | 10 | 30 | 50 | 70 | 
 | Nominal Sample Zone Temperature of 200 oC |  |  |  | 
Nominal Velocity, m/sec | 10 | 30 |  |  | 

## Slide 14: Other Sensor Exposures
Sensors were exposed to 8 hours of ammonia concentration of ~500 ppm
  Same Engine used but with urea injection
  FTIR was used to measure NH3 concentration
Sensors were exposed to 8 hours of 700C temperature
  High gas temperature diesel burner with DPF was used for this work
Sensors were exposed to sub-atmospheric pressure (0.75 atm) and positive pressure of (1.25 atm), (1 hour for each)
  This work was performed off-line

## Slide 15: Results-Example of Sensor Sensitivity After Multiple Exposures

## Slide 16: Results-Sensor Sensitivity Response at Different Velocities and different temperatures
35 m/sec 50 m/sec

## Slide 17: Correlation between Sensors and AVL MSS Soot Concentration (Steady-State (SS) Testing Only)
Steady-State Data
Steady-State Data

## Slide 18: Transient Response
Best Correlation Plot for FTP and NRTC transient cycles between a Sensor and the MSS

## Slide 19: Upcoming Year 2 of Consortium Activities
100,000 miles of durability using modern diesel engine (DOC+SCR+DPF+AMOX)
Cold Temperature Exposure -30°C
Shock & Vibration
RMI/RFI
Year 2 of the PSPD consortium provides excellent and cost-effective opportunity to evaluate spark-plug sized particle sensors for various applications

## Slide 20: Summary
Our work is showing the birth of spark-plug sized technology for sensing particles in engine exhaust
It is critical to continue the development of this technology with the help of engine and sensor manufactures and other interested stakeholders

## Slide 21
Southwest Research Institute®
For Questions, please contact Imad Khalek at Ikhalek@swri.org