## Slide 1: Preliminary Analysis of Heavy-Duty In-Use Program Gaseous Data for MY 2007-2009
3-28-2012
Larry Oeler, Justin Greuel, Phil Carlson
Compliance Division
U.S. EPA Office of Transportation & Air Quality

## Slide 2: Compliance Program Overview
Gaseous Pollutants
  Pilot Program conducted in 2005/2006
    Gave manufacturers/EPA experience with running the program
  Fully enforceable program started in 2007
    EPA made selections in late 2007
    Results due by end of 2009
PM
  Pilot 2007-2010
  Enforceable starting in 2011
3-28-2012

## Slide 3: Number of Families Tested
2007
  11 engine families
2008
  12 engines families
  7 manufacturers
2009
  18 engine families
  8 manufacturers

## Slide 4: Preliminary Analysis of Pass Ratios - 2007
Vehicle Result | Number of Vehicles | Range in “Pass Ratio” by Pollutant |  |  | 
 |  | HC | NOx | HC+NOx | CO
Pass | 20 | 99 - 100% | 93- 100% | - | 100%
 | 35 | - | - | 90- 100% | 100%
Fail | 1 | 100% | 7% | - | 100%
 | 2 | - | - | 0- 87% | 100%

## Slide 5: Preliminary Analysis of Pass Ratios - 2008
Vehicle Result | Number of Vehicles | Range in “Pass Ratio” by Pollutant |  |  | 
 |  | HC | NOx | HC+NOx | CO
Pass | 10 | 100% | 96 – 100% | - | 100%
 | 53 | - | - | 92 – 100% | 100%
Fail | 1 | 85% | - | - | -
 | 5 | - | - | Min 55% | -

## Slide 6: Preliminary Analysis of Pass Ratios - 2009
Vehicle Result | Number of Vehicles | Range in “Pass Ratio” by Pollutant |  |  | 
 |  | HC | NOx | HC+NOx | CO
Pass | 24 | 100% | 93 – 100% | - | 100%
 | 41 | - | - | 93 – 100% | 100%
Fail | 1 | - | 87% | - | -
 | 6 | - | - | 0- 82% | -

## Slide 7: Preliminary analysis of NTE Events - 2007

## Slide 8: Preliminary analysis of NTE Events - 2008
Chart: Number of vehicles vs number of NTE events 2008 MY engine families in manuf In-use program
| 0 | 1-10 | 11-20 | 21-30 | 31-40 | 41-50 | >50
Number of vehicles vs number of NTE events | 13 | 19 | 6 | 8 | 3 | 6 | 8

## Slide 9: Preliminary analysis of NTE Events - 2009
Chart: Number of vehicles vs number of NTE events 2009 MY engine families in manuf In-use program
| 0 | 1-10 | 11-20 | 21-30 | 31-40 | 41-50 | >50
Number of vehicles vs number of NTE events | 14 | 16 | 8 | 13 | 4 | 4 | 13