## Slide 1: Lessons and Applications in PEMS for on-highway Measurements
2012 PEMS Conference and Workshop - UCR/CE-CERT

## Slide 2: Background (Experience and Equipment)
Most of Cummins PEMS experience from conducting on-highway testing through the EPA HDIUT program
  Our group has performed over 350 in-use test missions
  Currently employee 4 test engineers in our group
Sensors SEMTECH-DS Gaseous Analyzer
  Good reliability and data yield (improvements have been implemented over the years)
  Updated NDUV are reliable and stable
  Difficult to pass CO linearity
Sensors PPMD (quartz crystal micro balance with proportional dilution)
  Gives quick results with no need for filter weighing
  Reliability has been an issue but has improved as we have worked through issues
  Careful attention to setup is required for quality data and good yield
  Remote dilution option offers installation flexibility
Proprietary data logger
  Ruggedized PC, data link adapter, and proprietary logging software
Honda 2k inverter generator (if needed)
  This is enough power to run the SEMTECH and PPMD standalone (no vehicle power) at steady state conditions

## Slide 3: Transporting Equipment to the Field
Started with a box truck
  Difficult to getting in and out and did not function well as a mobile lab/workshop
Moved to ¾ ton pickup pulling 16 foot tag trailer
  Worked fairly well and was in service for 6+ years, but outgrew the trailer size
Full ton cab-chassis pickup with 24 foot goose neck trailer
  7K generator for on site power
  Air-conditioned and heated to give PEMS equipment dry environment during service and checks
  Customer chassis accommodates boom crane for testing rig lifts

## Slide 4: Setup and Equipment Readiness
Good organization is key to expedient setup
  Have a plan for setup
  If you have more than on engineer or technician working the setup, logically group tasks for efficient work
Be sure your equipment is ready
  Analyzers don’t seem to like sitting idle. Best to have them running and fully checked out before the actual setup with the vehicle begins. Some of our missed testing opportunities in the past could have been avoided by better advanced checking of the equipment.
  Complete warm-up, calibrations and checks the day before testing is optimal
  Automating linearity can save you some time
    We automated the functions of a Horiba/STEC SGD-A10 push button divider

## Slide 5: Setup and Equipment Readiness (cont.)
Have proper equipment to lift PEMS
  Portable hand crank lifts work well for lifting PEMS into cab of other vehicle locations
Give yourself adequate time for equipment warm up and calibrations before vehicle mission launch.
  Although analyzers can warm up in less than an hour in some cases, you want extra time for complete stabilization and any unexpected issues.
  2 hours minimum is a good rule of thumb for people working setup.
  In some cases, leaving PEMS running over-night can save time

## Slide 6: Raw Exhaust Handling
Remote Diluter
PPMD
Rigid Exhaust Transport
No Remote Dilution, PPMD Exposed to outside elements
90 and 180 degree insulated smooth radius bends help orient the diluter for different applications
Flexible Exhaust Transport

## Slide 7: Running Test
Do a thorough review of real time data stream upon start of test/recording.
  You can often spot something that is wrong before the vehicle mission is launched and driver can not be stopped.
  VI data, concentrations, exhaust flow, power supply voltage etc.
  Do an rpm sweep and observe transient response and proportionality
It is advisable to continue monitoring data if possible or make frequent checks in order to catch any problems that might otherwise cause reason for retest (second shift day)
Avoid shutting vehicle off if possible.
  Continuous ECM data is easier to work with
  Minimizes risk of data logger failure

## Slide 8: Data Processing and Quality
Perform quality checks on data
    Review 1hertz report file for accuracy
    Check transport delay/time alignment
    Compare proprietary ECM data against CAN collect by analyzers
    Check torque curves for errors
    Check for transcription errors

## Slide 9: What can go wrong?
Can’t find adequate customers in time for compliance testing, customer procurement is a big driver in meeting schedule
  Start your customer procurement as early as possible
  Plan for customer driven delays
  Have back up options
PEMS breakdown
  Best if you can have back up units available if possible
  Arrange for PEMS supplier to provide support
Power supply to PEMS insufficient
  If running equipment without a generator, make sure your test vehicles charging system can keep up with the demand
Dilution Proportionality is poor
  Carefully setup and choose user set parameters i.e. maximum expected exhaust flow
  Eliminate any leaks in sampling systems

## Slide 10: What can go wrong? (cont.)
Vehicle Interface (ECM data) is intermittent, slow, or unavailable.
  Be sure to avoid any floating grounds with CAN communication equipment
Exhaust Flow Meter hardware doesn’t fit application
  Best if you can investigate the test vehicle in advance of the test day so that you can prepare for any unexpected exhaust configurations
  Stock a variety of exhaust hardware
Exhaust stack very rusty or deformed at silencer/after-treatment connection
  Use superior penetrating oil products on rusty bolts (off the shelf at local retailers are not as effective as commercial account type products)
  Use heat (torch) only if necessary and follow all safety precautions
  Cut off exhaust stack using “saws all” then extract the remaining piece of stack

## Slide 11: What can go wrong? (cont.)
Extreme environmental conditions (heavy rain, excessive heat, cold, vibration)
  Mount equipment in the cab as much as possible,
  When mounting outside environmental enclosures can protect from rain, but can be more difficult to cool in hot weather.
  Excessive heat or cold can limit equipments ability to regulate critical temperatures
    Avoid heat rejection sources from vehicle or insulate components as needed
  Implement vibration dampening as needed
Data processor or report compiling software makes error
  Develop data quality check/review process

## Slide 12: What recommendations/ improvements should be made?
PEMS reliability has improved substantially in recent years, however we hope for continued improvement
Any emerging technologies that allow for reduction in power consumption and size while not compromising measurement quality
Regulatory language proposed revisions
  CFR 86.1370-2007(g) after-treatment warm-up

## Slide 13
Questions?