## Slide 1
Development of a Mobile
Energy and Emissions
Telematic System (MEETS)
George Scora
University of California-Riverside
College of Engineering-
Center for Environmental Research and Technology
PEMS Conference
March 29, 2012

## Slide 2: Mobile Energy/Emissions Telematic System (MEETS) Concept

## Slide 3: Comprehensive Modal Emissions Model (CMEM)
Microscale emission model
  Developed at UCR CE-CERT
  Initially developed in the 1990’s
Sponsorship
  National Cooperative Highway Research Program (NCHRP)
  U.S. Environmental Protection Agency (EPA)
Developed to model vehicle emissions
  project level ( sec-by-sec)
Accurately reflect impacts of :
  Vehicle speed, acceleration, road grade, starting conditions, and secondary engine load

## Slide 4
vehicle activity (velocity trajectory)
calibration vehicle parameters
fuel consumption
emissions
general vehicle parameters
CMEM
grade (optional)
28 LDV
3 HDDV

## Slide 5: CMEM Emission Model Structure
Fuel is a function of Engine Power Demand and Engine Speed
Fuel rate is related to emissions through analysis based on measured data
Model Inputs
  Operating parameters - vehicle speed, road grade, accessory power, etc.
  Vehicle parameters – weight, gear ratios, calibrated emission parameters, etc.
Model Outputs
  Second–by–second emission data and fuel use

## Slide 6: Fuel Rate Calculation
k = engine friction term
N = engine speed
D = engine displacement
Pe = engine power
 = engine indicated efficiency
LHV = lower heating value of fuel
Pt = tractive power demand
 = drivetrain efficiency
Prun = running losses
Pacc = accessory power demand
S = engine-speed/vehicle-speed in top gear
RL = gear ratio in Lth gear
RT = gear ratio in top gear
v = vehicle speed

## Slide 7: Real-time Emission Modeling
Operating
variables
Vehicle
parameters
Power
demand
Engine
speed
Engine Control and Operating Conditions
Engine
-
out
emissions
Exhaust
after
-
treatment
Tailpipe
emissions,
f
uel use
Fuel
rate

## Slide 8: On-board Diagnostics (OBD)
Engine Control Unit (ECU)
Parameter Identification Data (PID)
  PID 05 = Engine Coolant Temperature (oC)
  PID 10 = Mass Air Flow Rate (g/s)
  PID 44 = Commanded Equivalence Ratio
  PID 3C = Catalyst Temperature Bank 1 Sensor 1 (oC)
  PID 0D = Vehicle Speed (km/h)

## Slide 9: OBD Parameters
Engine Coolant Temperature [PID 05]
  Used in MEETS to turn off engine cold start
  Replaces pseudo temperature value based on amount of fuel burned
Commanded Equivalence Ratio () [PID 44] and
Mass Air Flow (MAF) [PID 10]
  Used in MEETS to calculate fuel rate
  Replaces the core fuel rate in the CMEM model
Fuel Rate

## Slide 10: OBD Parameters
Catalyst Temperature
  Used in MEETS to approximate catalyst efficiency (CEe) for each criteria emission
  Replaces catalyst light off time parameters
where
Tc = current catalyst temperature
T0 = initial temperature
Tm = max/stable temperature
be = calibrated parameter for emission e
ne = calibrated parameters for criteria emission e

## Slide 11: Sources of Modeling Errors Bypassed
Second-by-second grade data
Meteorological conditions
  Wind*
Vehicle weight
  Fuel level, payload, passengers
Road conditions
Losses in drivetrain and engine
Accessory load
Driver gear shift behavior
Engine and catalyst warm-up characteristics

## Slide 12
UC Riverside ECO-Friendly Intelligent Transportation System (ECO-ITS) Test Bed Vehicle

## Slide 13
Example screenshots of MEETS on-board application

## Slide 14: MEETS Emission Outputs CO2
CO2 (g/s) | 
Measured | 2408.103
MEETS | 2472.424
% Difference | 2.7

## Slide 15: MEETS Emission Outputs CO
Cold Start
Hot Stabilized
CO (g/s) | 
Measured | 3.927
MEETS | 3.388
% Difference | 2.8

## Slide 16: MEETS Emission Outputs HC
Cold Start
Hot Stabilized
HC (g/s) | 
Measured | 0.514
MEETS | 0.483
% Difference | -5.9

## Slide 17: MEETS Emission Outputs NOx
Cold Start
Hot Stabilized
NOx (g/s) | 
Measured | 0.250
MEETS | 0.287
% Difference | 14.6

## Slide 18: Trade-offs
Cost
Performance
MEETS
PEMS
Ease of implementation
Modeled data not measured

## Slide 19: Conclusions
A mobile based emission estimation and reporting system can provide a unique set of real-time data which is valuable for traffic emission characterization
Improved emission estimations
  Bypass assumptions previously made to estimate fuel rate and engine operating conditions.
Various applications
  Low cost, easily implemented
  On-board driver feedback
  Broadcast energy/emissions from traffic for ITS
  Applicable to other platforms (i.e. Heavy Duty Diesel)
USDOT’s AERIS (Applications for the Environment: Real-time Information Synthesis) research program
  Real-time transportation data for environmental benefits

## Slide 20: Questions?