## Slide 1
Tips for High-Quality and Reliable PEMS Testing
Dan Carder
Center for Alternative Fuels, Engines and Emissions
Department of Mechanical and Aerospace Engineering
West Virginia University

## Slide 2: Areas of Data Quality
Pre-test Qualifications
Test Records
Installation
Pre-trip Inspection
Data Collection
Data Review
Post-test Qualifications
Quality Control/Quality Assurance Review

## Slide 3: Pre-Test Qualifications
Verifications of PEMS & subsystems, according to 40 CFR 1065 Subparts D and J. This involves setting up the analyzers with requisite gases and all ancillary hardware pertaining to the system, and allowing the equipment to reach operating temperature, generally 1-2 hours.
Zero/Span and Linearization (POST WARM-UP)
  Linearization/Regression (40 CFR 1065.307)
Interference Checks (40 CFR 1065 Subpart D)
  NOX Converter Efficiency/O2 Interference (40 CFR 1065.378 and .362)
Heated Sampling Line – Pressure and Temperature Traces
Thermocouple and Pressure Verifications
Exhaust Flow Rate Measurement – Verification
  Flow rate bench with a laminar flow element that is calibrated against NIST standards in order to verify flow rates measured by the PEMS unit.
System Filter Replacement

## Slide 4: Pre-Test Qualifications
PM Measurement System
  Flow rate and leak checks (NIST Traceability)
  Proportionality
  Meet (or Exceed) manufacturer’s recommendations
  Media handling and custody

## Slide 5: Test Records
“Sign-off” by Personnel
Electronic “Collection”
Maintain Custody Logs of Cal Gases, Calibration Instrumentation (Dates?)
Communication with QC/QA Officer

## Slide 6: Hardware Installation
Pre-test Visit for Unique Hardware Mounting Applications & ECM Data Log
  Lug Curve Request
  Warranty download** and fault codes
Ordinarily - 2-5 Hours
  Mostly dependent upon the difficulty of installing the calibration gas cylinders and the generator used to power the PEMS.
  Inductive heating
Vehicle Safety & Maintenance Inspection
Engine Oil & Fuel Samples
Take Pictures!!!!
  Hardware installation (exhaust, sample lines, aftertreatment)
  VIN tag
  Engine nameplate
  Odometers

## Slide 7: Hardware Installation
Human Appeal – This Is NOT What the Driver Likely Wants to Deal With
Driver Input
Driver Safety

## Slide 8: Pre-Trip Inspection
Make a Checklist
  Is Everything Tied-Down?
  Generator Fuel/Oil
  Sufficient Cal/Zero/FID Gas?
PEMS Warm-Up and Pre-trip Final System Checks and Calibrations
Verify all Temperatures and Sample Flow Rates
Record Curb Idle and Governed (High) Idle Flow Rates
“Wheels-on-the-Bus” Approach
Parking Lot Check??

## Slide 9: Data Collection
Sit-and-Wait…
Weather and Environmental Log
Periodic Data Review
Remote System Monitoring
  Data collection problems
  System malfunction
  > 3hours

## Slide 10: Data Review
Extremely Important, but the “Last Thing” One Wants to Do
Develop a System of Check Boxes – K.I.S.S.
Timeliness
Combination of Approaches
  Valid NTE Events?
  Pass/Fail Ratio
  Graphical Review (Carbon Balance, CO2/NOX, Flow Rates…..)
  Customized software for a more automated process
Pitfalls
  Exhaust flow rate
  Proportionality
  ECM data loss
  Analyzer flow rates
  Intermittent data
  Watch for “step changes”
  System temperatures

## Slide 11: Post-test Qualifications
Post-Test Pictures (Repeat of Odometer(s) and System Installation, Exhaust, etc.)
Zero/Span Drift
Post-Test Curb and Governed Idle Exhaust Flow Rates
PM Proportionality
Media Custody and Shipping
“Should I Stay or Should I Go?”
Pictures After Removal and Post-Test Vehicle Inspection & Sign-Off

## Slide 12: QC/QA Review
“External” Reviewer
Not just the “Last Step”
Establish a Checklist

## Slide 13
Conclusions
Document (Test Logs, PICTURES, Voice Notes, etc.)
Meet (or Exceed) PEMS Manufacturer’s Recommendations
No Such Thing as “Bad Data”
      Psychological Counseling???

## Slide 14: Thank You! Questions?
Center for Alternative Fuels, Engines and Emissions
CAFEE