## Slide 1: The Evolution of a Clean Energy Grid by 2035
Ed Smeloff
May 5, 2022
UC Riverside Solar Valley Conference

## Slide 2: What Might the California 2035 Grid Look Like
Resource Type | Baseline Clean Energy Resources (2019) (GW) | Incremental Resources in 2032 IRP (GW) | Incremental Resources in GridLab’s High Electrification/85% Clean Energy Scenario (GW) | Incremental Resources in CEC SB 100 2040 Core Scenario (GW)
Utility Scale Solar | 12.5 | 18.9 | 27.0 | 53.2
Customer Solar | 8.0 | 12.5 | 12.5 | 31.0
Land-Based Wind | 6.0 | 5.1 | 12.0 | 12.5
Offshore Wind | 0.0 | 1.7 | 4.0 | 5.3
Geothermal/Clean Firm | 2.7 | 1.2 | 2.0 | 0.1
Biomass | 1.3 | 0.0 | 0.0 | 0.0
Battery Storage | 0.2 | 14.8 | 15.0 | 32.1
Long Duration Storage | 3.7 | 1.0 | 4.0 | 4.0
Large-Scale Hydro | 12.3 | 0.0 | 0.0 | 0.0
Small Scale Hydro | 2.4 | 0.0 | 0.0 | 0.0
65% to 75% of all electricity comes from variable renewable energy sources (wind and solar)
85% to 95% of electricity is produced without emitting greenhouse gases
There is 10 to 20 times the amount of battery storage capacity connected to the grid
5 million electric vehicles are on the road in 2030, 100% of all new cars are electric by 2035
The majority of people heat their homes with electricity

## Slide 3: How Do We Keep the Lights On in 2035
Historically, peak demand was met by resources that could be turned on and off with relatively short notice.
The annual peak occurred during the summer between 4 pm and 6 pm, driven by high temperatures
Planning for peak needs by three regulated utilities and a handful of municipal utilities.
Up to half of the existing California fleet of methane-fired power plants could be retired
Almost all coal plants in the West will be retired
With rooftop solar the “net peak” has moved to the hours after the sun sets
There are now over 40 load serving entities responsible for planning and procuring clean energy resources.

## Slide 4: A New Framework for Reliability is Needed
A new framework needs to go beyond planning for annual peak demand.
With fewer gas power plants and more battery storage, shortfalls could occur later in the day.
Each load serving entity will need to plan and procure for the load they serve. They will also need to plan for battery charging.
Load will change as transportation and the heating of buildings are electrified.
Weather is becoming more extreme and harder to plan for.
How much system reliability is enough? What should the reserve margin be?
Critical loads may need more back up power if the grid itself become less reliable due to wildfires etc.

## Slide 5: Criteria for a New Reliability Framework
Durable: It needs to be adaptable to future grid conditions and emerging reliability needs;
Affordable: It needs to balance reliability with the costs of overprocurement;
Integrated: It must account for hourly dynamics of variable resources and battery charging requirements;
Customer Participation: It should encourage demand-side management and the development of distributed resources;
Longer term Planning: It should supports long-term resource planning by LSEs; and
Manageable: It needs to retain be relatively simple to administer, preserve bilateral transactions and enable CAISO market participation of all resources

## Slide 6: Visualizing a Chronological Framework Reliability
Chart: Hour
| 9-1 | 9-2 | 9-3 | 9-4 | 9-5 | 9-6 | 9-7 | 9-8 | 9-9 | 9-10 | 9-11 | 9-12 | 9-13 | 9-14 | 9-15 | 9-16 | 9-17 | 9-18 | 9-19 | 9-20 | 9-21 | 9-22 | 9-23 | 9-24
Nuclear | 1775 | 1775 | 1775 | 1775 | 1775 | 1775 | 1775 | 1775 | 1775 | 1775 | 1775 | 1775 | 1775 | 1775 | 1775 | 1775 | 1775 | 1775 | 1775 | 1775 | 1775 | 1775 | 1775 | 1775
Biogas | 208 | 208 | 208 | 208 | 208 | 208 | 208 | 208 | 208 | 208 | 208 | 208 | 208 | 208 | 208 | 208 | 208 | 208 | 208 | 208 | 208 | 208 | 208 | 208
Biomass/Wood | 456 | 456 | 456 | 456 | 456 | 456 | 456 | 456 | 456 | 456 | 456 | 456 | 456 | 456 | 456 | 456 | 456 | 456 | 456 | 456 | 456 | 456 | 456 | 456
Geothermal | 1238 | 1238 | 1238 | 1238 | 1238 | 1238 | 1238 | 1238 | 1238 | 1238 | 1238 | 1238 | 1238 | 1238 | 1238 | 1238 | 1238 | 1238 | 1238 | 1238 | 1238 | 1238 | 1238 | 1238
CC | 15384 | 15384 | 15384 | 15384 | 15384 | 15384 | 15384 | 15384 | 15384 | 15384 | 15384 | 15384 | 15384 | 15384 | 15384 | 15384 | 15384 | 15384 | 15384 | 15384 | 15384 | 15384 | 15384 | 15384
Cogen | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
CT | 6925 | 6925 | 6925 | 6925 | 6925 | 6925 | 6925 | 6925 | 6925 | 6925 | 6925 | 6925 | 6925 | 6925 | 6925 | 6925 | 6925 | 6925 | 6925 | 6925 | 6925 | 6925 | 6925 | 6925
ICE | 255 | 255 | 255 | 255 | 255 | 255 | 255 | 255 | 255 | 255 | 255 | 255 | 255 | 255 | 255 | 255 | 255 | 255 | 255 | 255 | 255 | 255 | 255 | 255
Hydro | 5002 | 5002 | 5002 | 5002 | 5002 | 5002 | 5002 | 5002 | 5002 | 5002 | 5002 | 5002 | 5002 | 5002 | 5002 | 5002 | 5002 | 5002 | 5002 | 5002 | 5002 | 5002 | 5002 | 5002
Interchange | 0 | 0 | 0 | 0 | 0 | 0 | 4000 | 4000 | 4000 | 4000 | 4000 | 4000 | 4000 | 4000 | 4000 | 4000 | 4000 | 4000 | 4000 | 4000 | 4000 | 4000 | 0 | 0
Wind Capacity | 2251.0326 | 2085.6698 | 1831.5425 | 1605.9857 | 1399.8797 | 1176.232 | 1013.3082 | 746.7595 | 426.7302 | 344.503 | 325.2864 | 337.6866 | 350.6147 | 454.5814 | 484.7003 | 562.486 | 742.1696 | 1016.6158 | 1604.411 | 1976.4391 | 2144.5794 | 2237.9608 | 2260.6434 | 2397.6856
Solar Capacity | -10.0024 | -10.002 | -10.0016 | -10.0013 | -10.001 | -9.2072 | 4502.8236 | 11877.2831 | 15579.575 | 17071.4671 | 17700.0007 | 17885.545 | 17494.9598 | 16854.8465 | 15708.8398 | 13688.6358 | 8867.8656 | 1574.7234 | -10.0744 | -10.0045 | -10.0041 | -10.0038 | -10.0033 | -10.0028
Excess Energy for
Shown Storage
Hydro
Fossil
Clean Firm
1-in-2 Load + 9% PRM